## Slide 1: Static Multiple-Issue (4.10)
Lecture 38
Notes: Last time?

## Slide 2: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice
§4.10 Parallelism via Instructions
Notes: We’re going to go over the high level ideas first, so the details will be missing. Then we’ll at least dig a little deeper with some more details.
What does 4 GHz mean? How many IPS for 4Ghz 1-way multiple-issue?

## Slide 3: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime
Notes: Sometimes the compiler can’t package them perfectly into slots b/c of dependencies…use what’s called a “nop”

## Slide 4: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated
Notes: We’ve already seen one example, what is it?
Speculate on loads: we often access arrays of elements…just guess the (address of ) next element

## Slide 5: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 6: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)
Notes: Q: What does ISA stand for?
Okay, that’s the high level for OOO execution, now let’s look in more detail at static dual issue

## Slide 7: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 8: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
Reorder instructions into issue packets
No dependencies within a packet
Possibly some dependencies between packets
  Varies between ISAs; compiler must know!
Pad with nop if necessary
Notes: MIPS was designed carefully, but with a different ISA we might have a different pipeline. For example, the memory access might actually come BEFORE the alu operation! Different hazards will result from that,…

## Slide 9: MIPS with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB
Notes: Notice we have to replicate the ALU, but not the memory, since an ALU/branch doesn’t access the memory

## Slide 10: MIPS with Static Dual Issue
Notes: There’s a bug in this figure…what is it? (Need to add 8 to PC…)
Also, notice just one ALU above registers…(first, what is this for?) why don’t new need to replicate this?
Why doesn’t the bottom ALU need muxes?

## Slide 11: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add $t0, $s0, $s1 lw $s2, 0($t0)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required