## Slide 1: Pipelining IMPLEMENTATION
4.6
Notes: Q: What was our analogy for pipelining? Give me a high-level overview of pipelining

## Slide 2: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture
Notes: Examples on p. 285
Stall on lw result
Bypass the first add result written into $t1
No stall or bypass required.

## Slide 3: MIPS Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards
Notes: Not only data hazards (WB) and control hazards (branch MEM), also just synchronization: time it takes to go down a wire vs. through the register file
e.g., don’t want instruction fetch to overwrite wires to registers if maybe registers are slow to use those values.

## Slide 4: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 5: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 6: IF for Load, Store, …

## Slide 7: ID for Load, Store, …

## Slide 8: EX for Load

## Slide 9: MEM for Load

## Slide 10: WB for Load
Wrong register number
Notes: Q: Anyone see a bug here?

## Slide 11: Corrected Datapath for Load

## Slide 12: EX for Store

## Slide 13: MEM for Store

## Slide 14: WB for Store

## Slide 15: Multi-Cycle Pipeline Diagram
Form showing resource usage
Notes: Q: There are two bugs in the shading of this diagram…what are they?
A1: add doesn’t need to use DM
A2: lw does need to use DM

## Slide 16: Multi-Cycle Pipeline Diagram
Traditional form
Notes: Can take a vertical “cross cut” to get a more detailed look at any given clock cycle…
For example, take cycle 5 here
Visualize that cross cut on next slide…

## Slide 17: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle
Notes: Here’s where we get to really bring everything together in our heads at once…
Now let’s go back to talking about the control signals…

## Slide 18: Pipelined Control (Simplified)
Notes: Control has the same kind of synchronization issues as the data path.
e.g., we generate the ALUSrc signal presumable in the ID stage, but need to make sure it’s not set until the EX stage.
so we should also include them in the pipeline registers.

## Slide 19: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation
Notes: Basically, save the multiplexor choices for a future stage (plus ALUop…)

## Slide 20: Pipelined Control

## Slide 21: Pipelining Details
4.7 - Detecting and handling data hazards
4.8 – Control hazards
4.9 – Exceptions
  Arithmetic overflow
  I/O device request
  Undefined operation
  Hardware malfunction
Notes: No time for the fun details :(

## Slide 22: Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 and $12,$2,$5 or $13,$6,$2 add $14,$2,$2 sw $15,100($2)
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling

## Slide 23: Dependencies & Forwarding
Notes: If you draw the diagram, forward whenever we would go back in time.

## Slide 24: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg
Notes: 1 – i.e. instruction is one ahead
2 – i.e. instruction is two ahead
We’re only going to consider forwarding to the EX stage, though in real life there is more forwarding.

## Slide 25: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0
Notes: Last part is just enforcing that we don’t write to the zero register; design choice.

## Slide 26: Forwarding Paths

## Slide 27: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
Notes: Otherwise 00 and use actual result from register file.

## Slide 28: Double Data Hazard
Consider the sequence:
  add $1,$1,$2 add $1,$1,$3 add $1,$1,$4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 29: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 30: Datapath with Forwarding
Notes: It’s starting to get too complicated to put everything up at once, so this is simplified; has branch stuff missing.

## Slide 31: Load-Use Data Hazard
Need to stall for one cycle
Notes: We still need to detect when this happens and do something about it!

## Slide 32: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs, IF/ID.RegisterRt
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.RegisterRt))
If detected, stall and insert bubble

## Slide 33: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Current instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for lw
    Can subsequently forward to EX stage

## Slide 34: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 35: Stall/Bubble in the Pipeline
Or, more accurately…

## Slide 36: Datapath with Hazard Detection

## Slide 37: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture

## Slide 38: Branch Hazards
If branch outcome determined in MEM
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)

## Slide 39: Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)

## Slide 40: Example: Branch Taken

## Slide 41: Example: Branch Taken

## Slide 42: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
…
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add $4, $5, $6
add $1, $2, $3
beq $1, $4, target
Can resolve using forwarding

## Slide 43: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add $4, $5, $6
lw $1, addr
beq $1, $4, target

## Slide 44: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
lw $1, addr
beq $1, $0, target

## Slide 45: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 46: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 47: 2-Bit Predictor
Only change prediction on two successive mispredictions
Notes: Start at 00 with strong predict not taken (maybe).

## Slide 48: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 49: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard
§4.9 Exceptions

## Slide 50: Handling Exceptions
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Save PC of offending (or interrupted) instruction
  In MIPS: Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: Cause register
  We’ll assume 1-bit
    0 for undefined opcode, 1 for overflow
Jump to handler at 8000 00180

## Slide 51: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Example:
  Undefined opcode: C000 0000
  Overflow: C000 0020
  …: C000 0040
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 52: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use EPC to return to program
Otherwise
  Terminate program
  Report error using EPC, cause, …

## Slide 53: Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  add $1, $2, $1
  Prevent $1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and EPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 54: Pipeline with Exceptions

## Slide 55: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in EPC register
  Identifies causing instruction
  Actually PC + 4 is saved
    Handler must adjust

## Slide 56: Exception Example
Exception on add in
  40 sub $11, $2, $4 44 and $12, $2, $5 48 or $13, $2, $6 4C add $1, $2, $1 50 slt $15, $6, $7 54 lw $16, 50($7) …
Handler
  80000180 sw $25, 1000($0) 80000184 sw $26, 1004($0) …

## Slide 57: Exception Example

## Slide 58: Exception Example

## Slide 59: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!

## Slide 60: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines