## Slide 1: Ch 3: Computer Arithmetic
Instructor: Robert Utterback
Lecture 25

## Slide 2: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 3: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0
Notes: When do we know if we had overflow?

## Slide 4: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 5: Overflow Detection
So how do we detect overflow for signed arithmetic?
0
1
1
1
0
0
1
1
+
1
0
1
0
1
1
1
0
0
1
0
1
1
+
0
1
1
1
1
1
0
7
3
1
-6
- 4
- 5
7
0
0
0
1
0
0
0
1
1
+
0
1
0
1
1
1
1
0
0
1
1
1
0
+
1
0
1
0
1
0
0
2
3
0
5
- 4
- 2
- 6
1
0
0
1
0
Notes: Check last carryIn vs. carryout.

## Slide 6: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve EPC value, to return after corrective action
Notes: By the way, depends on the language to utilize these…C does not!
Not the only way to handle overflow…

## Slide 7: Arithmetic for Multimedia
Saturating operations
  On overflow, result is largest representable value
    c.f. 2s-complement modulo arithmetic
  E.g., clipping in audio, saturation in video
Notes: e.g. volume knob/button

## Slide 8: Multiplication

## Slide 9: Sequential Version of Multiplication Algorithm and Hardware
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product

## Slide 10: Multiplication Hardware
First version of Multiplication Hardware
  32-bit multiplier
  64-bit ALU
  64-bit product (initialized to 0)
Notes: Unsigned numbers!

## Slide 11: Multiplication Hardware
Initially 0
Notes: Try an example: 2 * 3 with just 4 bits
Table:
Iteration #, Step (1a,2,3), Multiplier, Multiplicand, Product

## Slide 12: Example
2*3
Notes: #Now do an example with 8 bits: 0x62 * 0x12
What about -4 * 3 (don’t need to do the hardware process, you can work it out by hand)
Use 4 bits for multiplicand and multiplier, 8 for result.
Results is 40! Should be -12!