## Slide 1: 3.3: Multiplication
Instructor: Robert Utterback
Lecture 29

## Slide 2: Sequential Version of Multiplication Algorithm and Hardware
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
Notes: Which is the multiplier, which is multiplicand?

## Slide 3: Multiplication Hardware
First version of Multiplication Hardware
  32-bit multiplier
  64-bit ALU
  64-bit product (initialized to 0)
Notes: Unsigned numbers!

## Slide 4: Multiplication Hardware
Initially 0
Notes: Try an example: 2 * 3 with just 4 bits
Table:
Iteration #, Step (1a,2,3), Multiplier, Multiplicand, Product

## Slide 5: Example
2*3
Notes: Now do an example with 8 bits: 0x62 * 0x12

## Slide 6: Signed Multiplication
Option 1:
  Multiply with absolute value
  Compute the correct sign at end
Option 2:
  Previously algorithm almost works
  “Sign extend” when shifting

## Slide 7: Optimized Multiplier
Refined Multiplier
  32-bit multiplicand and ALU
  Multiplier is placed in the right half of the product register
  64-bit product register

## Slide 8: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low
Notes: Multiplier is in the right half of the product register.

## Slide 9: Alternative Multiplier
One 32-bit adder for each bit of multiplier
Input1 is multiplicand AND multiplier bit
Input2 is output of previous adder
“Chain” of adders, 32 high

## Slide 10: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel
Notes: Not correct!

## Slide 11: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd
Notes: This last is a pseudoinstruction

## Slide 12: Back to the Example
A better way to do 2*3?
  3 << 1
  using SLL
Almost all compilers will perform a strength reduction optimization by replacing multiplication of power of 2 by shifting

## Slide 13: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 14: Division Hardware
Initially dividend
Initially divisor in left half
First version of Division Hardware
  32-bit quotient
  64-bit ALU
  64-bit remainder
Notes: Divisor starts in left half of divisor register, remainder initialized to dividend

## Slide 15: First Version Division Hardware
Initially dividend
Initially divisor in left half
Notes: Example: Fill out a table for 7/2
Table:
Iteration, Step (1,2b,3), Quotient, Divisor, Remainder

## Slide 16: Example
7/2