## Slide 1: Instructions: Language of the Computer (Ch 2)
Instructor: Robert Utterback
Lecture 13

## Slide 2: Memory Operand Review
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
Notes: Exercise: Write the MIPS code for this…

## Slide 3: Adding Constants Review
C code:
a = b + 42;
a in $s0, b in $s1
Notes: Addi $s0, $s1, 42

## Slide 4: Review
C code:
A[2]++; // add one to A[2]
A in $s0
Notes: lw $t0, 8($s0)
addi $t0, $t0, 1
sw $t0, 8($s0)

## Slide 5: Review
What does lb do?
  lb $t0, 0($s2)
T/F: The address (base register + offset) to lb must be a multiple of 4.
Notes: Loads a byte from memory
False, but the hardware will align it

## Slide 6: Instructions so far
add $t0, $s1, $s2
sub $s0, $t0, $t1
lw $t0, 32($s3)
sw $t1, 48($s3)
addi $s3, $s3, 4
+ lb,lbu,lh,lhu
Also: sb,sh
Also: addu, subu, addiu

## Slide 7: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: There are a few different formats; here’s one. The “op” and “funct” *together* tell us exactly what instruction is happening.
You don’t have to memorize stuff like this – it’s on your ”green sheet” and I always let you use it on exams.

## Slide 8: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: Sub is op=0, funct=34., NOR=27, OR=25 (funct)
Most R format instructions have op=0 (I only know of 1 that does not)
So these are long strings of bits…difficult to read. But we have a bit of a shortcut.

## Slide 9: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000
Notes: It’s way too messy to always deal with bit strings…

## Slide 10: Example
What instruction is:
012a 8020 ?
add $s0, $t1, $t2
Notes: 0000 0001 0010 1010 1000 0000 0010 0000
000000 01001 01010 10000 00000 100000
Op = 0
Rs = 9
Rt = 10
Rd = 16
Shamt = 0
Funct = 32
So this is an add instruction.

## Slide 11: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Notes: If you didn’t have this extra format, you either (1) couldn’t specify constants directly (would have to load them from memory), or (2) would re-use a register field for a constant (I-format). But then you only have 2^5 = 32 options for the constant. Here you’re still limited, but it’s a little bit better because you can go up to 2^16. Of course, you could make your instructions bigger to accommodate larger constants, but then, well, your instructions are larger.
There are always trade-offs in design, and you will need to make compromises.

## Slide 12: Mini Green Sheet
MIPS instructions
  R:
  I:
Register numbers
  $t0 – $t7 : 8 – 15, $t8 – $t9 : 24 – 25
  $s0 – $s7 : 16 – 23, $zero : 0
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Notes: With a single exception, when op=0 it’s in R format

## Slide 13: MIPS I-format Instructions
Which is rs and which is rt?
  addi $t5, $s4, 5
  lw $t0, 24 ($s0)
  sw $t1, 16 ($t8)
  addi $t0, $t1, -191
rt becomes destination for many I format…
Notes: Addi: rs = s4, rt = t5
Lw: rs = s0, rt = t0
Sw: rs = t8, rt = t1
Addi: rs = t1, rt = t0

## Slide 14: Convert into MIPS
Are these R type or I type?
  2231 0080
  8e50 0008
  0230 8820
  ae51 0000
Notes: 22 = 00100010 = 001000 = 8 = addi = I
8e = 10001110 = 100011 = 35 = 23_hex = lw = I
02 = 00000010 = 000000 = 0 = add (20 = 00100000 = 100000 = 32) = R
Ae = 10101110 = 101011 = 43 = 2b_hex = sw = I
Note that greensheet uses hex to represent I-format opcodes!

## Slide 15: In Class Exercises
Convert the following MIPS instructions into Machine Instructions
add $t1, $t2, $t3
addi $t5, $s3, 5
lw $t4, 200($s3)
Notes: 0 10 11 9 0 32 = 0000 0001 0100 1011 0100 1000 0010 0000 = 014b 4820
8 19 13 5 = 0010 0010 0110 1101 0000 0000 0000 0101 = 226d 0005
35 19 12 200 = 1000 1110 0110 1100 0000 0000 1100 1000 = 8e6c 00c8