## Slide 1: Measuring Performance
Instructor: Robert Utterback
Lecture 2
Notes: Pace of course: let me know if too fast/slow
Ask questions! Experienced professors are good at noticing when students are confused. I’m still working on it.
Read the syllabus carefully -- I'm not going to hold your hand.

## Slide 2: Review
What are the steps to transform a program written in C into a representation that is directly executed by a computer processor?

## Slide 3: An Analogy
Which airplane is the best?

## Slide 4: An Analogy
Which airplane is the best?

## Slide 5: Defining Performance
Which airplane has the best performance?
§1.6 Performance
Notes: Section 1.6

## Slide 6: Answer
That depends on …
  If performance means
    “the least time of transferring 1 passenger from one place to another”
      Concorde
    “the least time of transferring 450 passenger from one place to another”
      Boeing 747
Performance can be defined in different ways

## Slide 7: Response Time and Throughput
Response time (AKA Execution Time)
  How long it takes to do a task
Throughput (AKA Bandwith)
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…
Notes: Faster processor: reduces response time AND increases throughput
More processors: Increase throughput, same response time (probably, unless there is a backlog of tasks)

## Slide 8: Performance and Execution Time
Performance

## Slide 9: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 10: Class Exercise
Computer B runs a program in 24 seconds.
Computer A runs the program 1.2 times faster.
How long does the program take on computer A?
Notes: Perf_A / Perf_B = 1.2 = Time_B / Time_A
=> Time_A = Time_B / 1.2 = 24 * 5/6 = 20 s

## Slide 11: Measuring Execution Time
Elapsed (Wallclock) time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
    User CPU time: CPU time spent in a program itself
    System CPU time: CPU time spent in the OS performing task on behalf of the program
  Different programs are affected differently by CPU and system performance
Notes: When we talk about elapsed time for a single program, we typically mean total response time on an unloaded machine.

## Slide 12: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 13: CPU Time

## Slide 14: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count
Notes: Increasing clock rate
=> shorter clock period
=> Shorter instructions, but more of them
=> More total clock cycles
Reduce number of clock cycles
=> Fewer instructions,
but they become longer since they must be more complicated
=> longer clock period
=> reduced clock rate

## Slide 15: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?
Notes: CPU Time = Clock cycles / Clock Rate

## Slide 16: Instruction Set Architecture
Instruction Set Architecture (ISA)
  An abstract interface between the hardware and the lowest-level software that encompasses all the information necessary to write a machine language program that will run correctly
    Repertoire of instructions
    Registers
    Memory access
    I/O

## Slide 17: Clock Cycles per Instruction (CPI)
Clock Cycles per Instruction (CPI)
  Average number of clock cycles per instruction for a program

## Slide 18: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 19: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 20: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 21: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1:
  IC
  Clock Cycles
  Avg. CPI
Sequence 2:
  IC
  Clock Cycles
  Avg. CPI

## Slide 22: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 23: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture
Notes: Response time and Throughput
Performance measures: CPI, IC
Performance = 1/Execution Time

## Slide 24: Power Trends
In CMOS IC technology
§1.7 The Power Wall
×1000
×30
5V → 1V
Notes: Section 1.7
Power and clock rate increased until we hit a wall...too much power, plus this causes heat which you have to cool
CMOS = Complementary metal oxide semiconductor
Capacitive load: resist changes in voltage
Frequency of transitions for the transistor

## Slide 25: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
Notes: We can’t reduce voltage further
We can’t remove more heat

## Slide 26: The Power Wall
Reduce Voltage
  With lower voltage, transistors “leak”. Currently responsible for 40% of the power consumption
Reduce Heat
  More powerful cooling
How else can we improve performance?

## Slide 27: Uniprocessor Performance
§1.8 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency
Notes: Section 1.8

## Slide 28: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization