## Slide 1: Instructions
Instructor: Robert Utterback
Lecture 13

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction
Notes: Instructions: commands that a computer can understand

## Slide 3: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
§2.3 Operands of the Computer Hardware
Notes: For now, just s and t. We’ll get to why these names, and use the rest of the registers, in 2.8.

## Slide 4: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4

## Slide 5: Instructions so far
add $t0, $s1, $s2
sub $s0, $t0, $t1
lw $t0, 32($s3)
sw $t1, 48($s3)

## Slide 6: Memory Operand Review
C code:
A[10] = c + B[4];
  c in $s0, base address of A in $s2, base address of B in $s3
Compiled MIPS code:
lw $t0, 16($s3) # load word add $t0, $s0, $t0 sw $t0, 40($s2) # store word
Notes: Exercise: what about A[2] = A[0] + A[1], with base of A in $s0?

## Slide 7: What does this do?
add $s1 $zero $zero
lw $s0 4($s2)
add $s1 $s1 $s0
lw $s0 8($s2)
add $s1 $s1 $s0
lw $s0 12($s2)
add $s1 $s1 $s0
lw $s0 16($s2)
add $s1 $s1 $s0
sw $s1 0($s2)

## Slide 8: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!
Notes: Simple example: a single registers, two data words. Need to do two operations on one, just one on the other.

## Slide 9: Adding Constants
C code:
a = b + 1;
Data must be in registers
Load from memory just for a constant?

## Slide 10: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction
Notes: Although in some sense, this IS still loading from memory, since the instructions are stored in memory. Surprise!

## Slide 11: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 12: Practice
Write the following in MIPS
  $t0 = $t1 + 48

## Slide 13: Representing Numbers (review)
Section 2.4

## Slide 14: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers
Notes: Quick review of section 2.4: we’ve already seen this stuff. Read 2.4 if you need a review or didn’t quite catch it the first time.

## Slide 15: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 16: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 17: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 18: Sign Extension
Representing a number using more bits
  Ex: load 8-bit value into 16-bit registers
  Preserve the numeric value
Examples: 8-bit to 16-bit
  +2: 0000 0010 =>
  –2: 1111 1110 =>

## Slide 19: Sign Extension
Representing a number using more bits
  Ex: load 8-bit value into 16-bit registers
  Preserve the numeric value
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 20: Sign Extension
Representing a number using more bits
  Ex: load 8-bit value into 16-bit registers
  Preserve the numeric value
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
In MIPS instruction set
  lb, lh: extend loaded byte/halfword
Replicate the sign bit to the left
Notes: As oppose to lbu and lhu, which will fill with 0s always.

## Slide 21: Representing Instructions
Section 2.5

## Slide 22: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23
§2.5 Representing Instructions in the Computer

## Slide 23: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 24: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: By the way, why 5 bits for the registers?
So these are long strings of bits…difficult to read. But we have a bit of a shortcut.

## Slide 25: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000
Notes: It’s way to messy to always deal with bit strings…

## Slide 26: Example
What instruction is:
012a 8020 ?
add $s0, $t1, $t2
Notes: 0000 0001 0010 1010 1000 0000 0010 0000
000000 01001 01010 10000 00000 100000
Op = 0
Rs = 9
Rt = 10
Rd = 16
Shamt = 0
Funct = 32
So this is an add instruction.