## Slide 1: Instructions
Instructor: Robert Utterback
Lecture 14

## Slide 2: Instructions so far
add $t0, $s1, $s2
sub $s0, $t0, $t1
lw $t0, 32($s3)
sw $t1, 48($s3)
addi $s3, $s3, 4
+ lb,lbu,lh,lhu
Also: sb,sh
Also: addu, subu, addiu

## Slide 3: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
§2.5 Representing Instructions in the Computer

## Slide 4: MIPS R-format Instructions
add
  op = 0
  funct = 32
sub
  op = 0
  funct = 34
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 5: Example
What instruction is:
0211 4022 ?
add $s0, $t1, $t2
Notes: 0000 0010 0001 0001 0100 0000 0010 0010
000000 10000 10001 01000 00000 100010
Op = 0
Rs = 16
Rt = 17
Rd = 8
Shamt = 0
Funct = 34
So this is: sub $t0, $s0, $s1

## Slide 6: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Notes: If you didn’t have this extra format, you either (1) couldn’t specify constants directly (would have to load them from memory), or (2) would re-use a register field for a constant (I-format). But then you only have 2^5 = 32 options for the constant. Here you’re still limited, but it’s a little bit better because you can go up to 2^16. Of course, you could make your instructions bigger to accommodate larger constants, but then, well, your instructions are larger.
There are always trade-offs in design, and you will need to make compromises.

## Slide 7: Mini Green Sheet
MIPS instructions
  R:
  I:
Register numbers
  $t0 – $t7 : 8 – 15, $t8 – $t9 : 24 – 25
  $s0 – $s7 : 16 – 23, $zero : 0
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Notes: With a single exception, when op=0 it’s in R format

## Slide 8: MIPS I-format Instructions
Which is rs and which is rt?
  addi $t5, $s4, 5
  lw $t0, 24 ($s0)
  sw $t1, 16 ($t8)
  addi $t0, $t1, -191
Notes: Addi: rs = s4, rt = t5
Lw: rs = s0, rt = t0
Sw: rs = t8, rt = t1
Addi: rs = t1, rt = t0

## Slide 9: Convert into MIPS
Are these R type or I type?
  2231 0080
  8e50 0008
  0230 8820
  ae51 0000
Notes: 22 = 00100010 = 001000 = 8 = addi = I
8e = 10001110 = 100011 = 35 = lw = I
02 = 00000010 = 000000 = 0 = add (20 = 00100000 = 100000 = 32)
Ae = 10101110 = 101011 = 43 = sw

## Slide 10: In Class Exercises
Convert the following MIPS instructions into Machine Instructions
add $t1, $t2, $t3
addi $t5, $s3, 5
lw $t4, 200($s3)
Notes: 0 10 11 9 0 32
8 19 13 5
35 19 12 200

## Slide 11: What I want you to do
Finish HW 2
Read Ch. 2