## Slide 1: Character Data
Instructor: Robert Utterback
Lecture 20

## Slide 2: Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword

## Slide 3: Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People
Notes: A mapping from numbers to characters. First 7 bits of Unicode are ASCII, which is convenient.

## Slide 4: String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
  Addresses of x, y in $a0, $a1
  i in $s0
Notes: In C++, we have a nice string class, which handles most things for us automatically.
This is actually pretty nasty C code…when you start to write code like this you can call yourself a C wizard.
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 5: String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 6: Handling Large Immediate constants
Notes: e.g. Constants and addresses

## Slide 7: 32-bit Constants
0000 0000 0111 1101 0000 0000 0000 0000
Most constants are small
  16-bit immediate is sufficient
For the occasional 32-bit constant
lui rt, constant
  Copies 16-bit constant to left 16 bits of rt
  Clears right 16 bits of rt to 0
lui $s0, 61
0000 0000 0111 1101 0000 1001 0000 0000
ori $s0, $s0, 2304
§2.10 MIPS Addressing for 32-Bit Immediates and Addresses
Notes: 61 -> 007d 0000
2304 = 0900
Ori: 007d 0900 = 8192000
Note: The assembler can handle this for us…

## Slide 8: Assembler Pseudoinstructions
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: figments of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary
Notes: In some sense, we’re defining another language just slightly more convenient than assembly…
Don’t use these on the exam…