## Slide 1: Combinational Logic (B.3)
Instructor: Robert Utterback
Lecture 6
Notes: In this lecture you’re going to learn a lot of new things: the basic building blocks of a computer. We’ll slowly combine these to learn how many components of a computer are built up.

## Slide 2: Review
= ?
What is a multiplexor?
Convert to sum of products
Notes: First, use DeMorgan’s
Third: AB~C

## Slide 3: Programmable Logic Array
Programmable Logic Array (PLA)
  Two stages of logic
    An array of AND gates (product terms)
    An array of OR gates
Notes: Common logic implementation called PLA
AND, OR *plane*
We can use a PLA to directly implement the truth table of a set of logic functions easily.

## Slide 4: PLA Example
Considering the following table, implement the PLA for D, E, F
Notes: For a particular output, look at each 1 value. Then AND together the inputs. OR together everything that produces a 1 value in this column. Notice that we don’t need to represent 0s at all, e.g. the first row.

## Slide 5: PLA Representation
Notes: Two things make PLAs efficient:
(1) only truth table entries that produce a true value for at least one output need any logic gates!
(2) Each different product term will have only one entry in the PLA, even if the product term is used in multiple outputs

## Slide 6: Another PLA Representation
Dot in the AND plane
  Input, or its inverse, occurs in the product term
Dot in the OR plane
  Corresponding product term appears in the corresponding output
Notes: Another form of structured logic used to implement logic functions is…

## Slide 7: Read Only Memory
Read Only Memory (ROM)
  Has a set of locations that can be read
  Contents of these locations are fixed
Programmable ROM (PROM)
  Can be burnt using a device called a “ROM programmer”
Erasable Programmable Read Only Memory (EPROM)
  Data in the ROM can be deleted under ultra-violet rays
EEPROM (Electrically Erasable Read Only Memory)
  Data in the ROM can be erased by a simple electric current
Notes: Called memory b/c it has a set of locations that can be read from
However, the contents of these locations are “fixed”, in that at least they are not easily changeable at running time

## Slide 8: ROM
Height
  m inputs
  2m addressable entries (input lines)
Width
  n outputs (functions)
  2n output bits
mxn is the shape of the ROM
Notes: Can encode logic functions basically as a lookup table: n functions with m inputs. Assign a number (label) to each possible input combination, that’s your address.

## Slide 9: ROMs and PLAs
PLA is partially decoded
ROM is fully decoded
  Contains a full output word for every possible input combination
  Always contain at least as many entries as the PLA
PLA (7 entries)
ROM (8 entries – 1 unused)
Notes: As the number of inputs grows, the number of entries in ROM grows exponentially. For most logic functions, the size of PLAs grows much more slowly, so it’s more efficient to use PLAs.
However, if your logic function changes, you made need to build a new PLA. A PROM can be changed to implement any logic function with the same # inputs and outputs.

## Slide 10: Don’t Care
Don’t Care
  We don’t care about the actual values
Output Don’t Care
  We don’t care about the value of an output for some input combination
Input Don’t Care
  An output only depends on some of the inputs
Advantages of Don’t Care
  Easier to optimize the implementation of a logic function
Notes: Basically this gives you lots of flexibility in how you can implement such a circuit, since for these don’t cares the output could be either 0 or 1.

## Slide 11: Example of Don’t Cares
Original Truth Table
Notes: First, note that when D and E are true, we don’t care about F, so we can put X’s there…
A is in both the top two statements – if A is true, it forces both D and E to be true and we don’t care about B and C. This actually lets us remove multiple rows! Now if both B and C are true, then we don’t care about A.

## Slide 12: Example of Don’t Cares
Output Don’t Cares
Input Don’t Cares
Notes: Don’t Care terms are key to getting efficient logic function implementations; they give us a lot of flexibility. These days, though, design tools can help you do logic minimization very well, without a lot of knowledge.

## Slide 13: Array of Logic Elements
Bus
  In logic design, a collection of data lines that is treated together as a single logical signal
  Shared collection of lines with multiple sources
32-bit wide 2-to-1 multiplexor
Notes: We’re almost to ALUs now. One other thing we need to talk about: “arrays” of logic elements.
Notice the difference between this and an n-to-1 multiplexor, say 32-to-1. Who can explain the difference to me?

## Slide 14: A simple Arithmetic Logic Unit (B.5)
Notes: In this lecture you’re going to learn a lot of new things: the basic building blocks of a computer. We’ll slowly combine these to learn how many components of a computer are built up.

## Slide 15: Bit, Byte, and Word
1 Bit – 0 or 1
1 Byte – 8 bits
1 Word – N bytes (in general)
  4 bytes in a word (in our book)

## Slide 16: Most Significant Bit and Least Significant Bit
Most Significant Bit (High-Order Bit)
  The bit position having the greatest value
  Usually the left-most bit
Least Significant Bit (Low-Order Bit)
  The bit position having the smallest value
  Usually the right-most bit
Notes: Some terminology…

## Slide 17: Binary Representation of Integers
Unsigned Integers
  0 and positive integers only
Signed Integers
  0, negative, and positive integers
  Three ways
    Sign-Magnitude
    1’s Complement
    2’s Complement
Notes: We talked before about representing positive integers…we call those “unsigned.”
But obviously sometimes we want to talk about negative numbers. There are a few different ways to represent negative numbers.
Some of this is foreshadowing chapter 2, but it will help to understand how the Adder works.

## Slide 18: Unsigned Integers
Unsigned Integers
  Consider a word = 4 bytes
  Can represent numbers from 0 to 4294967295
  Decimal:
  0 to 232-1
  Binary:
  0 to 111111111111111111111111111111112
Example
671210 = 00000000 00000000 00011010 001110002
Notes: Now, take a moment: you’re a Cpu designer 50 years ago and you need to compute with negative numbers. How would you implement signed integers (the ability to have both positive and negative numbers)?

## Slide 19: Signed Integer – Sign Magnitude
Sign Magnitude
Use the most significant bit of the word to represent the sign
  0 – Positive
  1 – Negative
Rest of the number is encoded in magnitude part
Example
  671210 = 00000000 00000000 00011010 001110002
  -671210 = 10000000 00000000 00011010 001110002
Two representations of 0
  0 = 00000000 00000000 00000000 00000000
  -0 = 10000000 00000000 00000000 00000000
Cumbersome in Arithmetic
Notes: Think about adding a negative number and a positive number

## Slide 20: 1’s Complement
1’s Complement
  Negative number is stored as bit-wise complement of corresponding positive number
  Use the most significant bit of the word to represent the sign
    0 – Positive
    1 – Negative
  Example
  671210 = 00000000 00000000 00011010 001110002
  -671210 = 11111111 11111111 11100101 110001112
  Still two representations of zero
  0 = 00000000 00000000 00000000 00000000
  -0 = 11111111 11111111 11111111 11111111

## Slide 21: 2’s Complement
2’s Complement
  Positive number represented in the same way as sign-magnitude and 1’s complement
  Negative number obtained by taking 1’s complement of positive number and adding 1
  671210 = 00000000 00000000 00011010 001110002
  1’s comp: -671210 = 11111111 11111111 11100101 110001112
  2’s comp: -671210 = 11111111 11111111 11100101 110010002
  One version of 0
  Convenient in arithmetic

## Slide 22: Integer Addition
Example: 7 + 6
00000000 00000000 00000000 00000111
+ 00000000 00000000 00000000 00000110
00000000 00000000 00000000 00001101
§3.2 Addition and Subtraction
Notes: So let’s add two numbers…exercise with at least one negative number.

## Slide 23: Integer Subtraction
Subtraction is actually an addition
Example: 7 – 6 = 7 + (-6)
2’s complement
00000000 00000000 00000000 00000111
+ 11111111 11111111 11111111 11111010
00000000 00000000 00000000 00000001
Notes: Rather than implementing both add and subtract, we can save some transistors and just implement add.
This also exhibits how we don't need to treat negative numbers any differently when using 2's complement!

## Slide 24: Overflow
Overflow if result out of range
  Adding +value and –value operands, no overflow
  Adding two +value operands
    Overflow if result sign is -
  Adding two –value operands
    Overflow if result sign is +
Notes: With an 8-bit word, let’s try to add 125 and 4.
Common bug of averaging two numbers.

## Slide 25: Arithmetic Logic Unit
Arithmetic Logic Unit (ALU)
  Heart of a CPU
  Operations
    Arithmetic operations
      Addition
      Subtraction
    Logical operations
      NOT
      AND
      OR