## Slide 1: The Memory Hierarchy
Chapter 5
Notes: On a write hit, one thing we could do it always write the result back to memory. What is this called (write-through)
What’s the alternative? (write-back, which only writes back to memory when a block is kicked out of memory)
It’s a waste to write back to memory if we haven’t changed the block since it came into cache. How do we handle this? (dirty bit)

## Slide 2: Set Associative Cache Organization
Notes: But as soon as we allow multiple ways, we have a new choice to make.
When we need to kick something out of cache, which way do we choose?

## Slide 3: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 4: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L1 cache usually smaller than a single cache
  L1 block size smaller than L2 block size
Notes: The l2 (or l3) is kind of like your last-ditch/resort effort

## Slide 5: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation
Notes: Misses depend on memory access patterns, including algorithm behavior and compiler optimizations

## Slide 6: The Hamming SEC Code
Hamming distance
  Number of bits that are different between two bit patterns
Minimum distance = 2 provides single bit error detection
  E.g. parity code
Minimum distance = 3 provides single error correction, 2 bit error detection
Notes: I’m actually not going to cover any more of this. There’s some more details in the book, but I doubt it will be useful to you all, so let’s just skip it.

## Slide 7: Virtual Machines
Host computer emulates guest operating system and machine resources
  Improved isolation of multiple guests
  Avoids security and reliability problems
  Aids sharing of resources
Virtualization has some performance impact
  Feasible with modern high-performance comptuers
Examples
  IBM VM/370 (1970s technology!)
  VMWare
  Microsoft Virtual PC
§5.6 Virtual Machines
Notes: Who’s heard of VirtualBox? Similar concept is containers; might have heard of Docker.
Amazon and lots of cloud providers are using these heavily.

## Slide 8: Virtual Machine Monitor
Maps virtual resources to physical resources
  Memory, I/O devices, CPUs
Guest code runs on native machine in user mode
  Traps to VMM on privileged instructions and access to protected resources
Guest OS may be different from host OS
VMM handles real I/O devices
  Emulates generic virtual I/O devices for guest

## Slide 9: Example: Timer Virtualization
In native machine, on timer interrupt
  OS suspends current process, handles interrupt, selects and resumes next process
With Virtual Machine Monitor
  VMM suspends current VM, handles interrupt, selects and resumes next VM
If a VM requires timer interrupts
  VMM emulates a virtual timer
  Emulates interrupt for VM when physical timer interrupt occurs
Notes: e.g. timer for scheduling multiple processes

## Slide 10: Instruction Set Support
User and System modes
Privileged instructions only available in system mode
  Trap to system if executed in user mode
All physical resources only accessible using privileged instructions
  Including page tables, interrupt controls, I/O registers
Renaissance of virtualization support
  Current ISAs (e.g., x86) adapting

## Slide 11: The Problem with Memory
Two programs running at the same time
  Prog A has bug – bad pointer value
  Overwrites into memory used by Prog B!
Buying from Amazon.com
  Enter CC info into browser
  Another program reads the browser memory and gets CC info
Some memory locations reserved for OS, communication with devices, etc.
Some programs need more memory than a machine has
  But we have plenty of disk space
§5.7 Virtual Memory

## Slide 12: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 13: Address Translation
Fixed-size pages (e.g., 4K)

## Slide 14: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 15: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk
Notes: Each process has its own page table, usually allocated in operating system memory space
So the page table register just points to the page table

## Slide 16: Translation Using a Page Table
Notes: Notice that the physical page number means something different depending on the valid bit.
If valid, it’s the physical address in memory
If not, it’s a disk address.

## Slide 17: Mapping Pages to Storage

## Slide 18: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 19: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 20: Fast Translation Using a TLB
Notes: Draw a matrix:
TLB hit vs. miss x page table valid vs. not valid
If TLB hit, must be in physical memory

## Slide 21: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction