## Slide 1: Memory Elements (B.8)
Instructor: Robert Utterback
Lecture 11

## Slide 2: Logistics
HW 2 went out on Wednesday (see email)
Start early!
Come to office hours/tutoring

## Slide 3: Four 4-bit ALUs with Carry Lookahead to form a 16-bit adder
Notes: Given some bits a_i and b_i, how to compute p_i and g_i?
What are the steps to do this two-layer carry lookahead adder?

## Slide 4: Clock Cycle
Clock cycle time (clock period)
  Two portions
    Clock is high
    Clock is low
Edge-triggered clocking
  All state changes occur on a clock edge

## Slide 5: State Element and Valid State
State Element
  A memory element
Signals written into state elements must be valid when the active clock edge occurs
  Valid means stable (not changing)
    Will not change again until the inputs change
Synchronous System
  A memory system that employs clocks and where data signals are read only when the clock indicates that the signal values are stable

## Slide 6: Read and Write in one cycle
Edge-triggered methodology allows a state element to be read and written in the same clock cycle
  Read the value of a state element
  Send it through some combinational logic
    Value does not change during the clock cycle
  Write it back to the same state element
  All in one cycle

## Slide 7: Memory Elements
Memory Elements
  Store States
  Output depends on
    The inputs, and
    The value stored in the memory element
Elements
  Flip-Flops
  Latches
  Registers
  Register Files
  SRAMS
  DRAMS

## Slide 8: Set-Reset Latch (S-R Latch)
A pair of cross-coupled NOR gates
  Unclocked
    Do not have a clock input
  Can store an internal value
    Q represent the current state
Notes: Draw a truth table for this (inputs are Q_old, ~Q_old, R and S, outputs are Q_new and ~Q_new)

## Slide 9: S-R Latch (Cont.)
S=0 and R=0
  Previous State is stored
S=1 and R=0
  Q=1 and ~Q=0
S=0 and R=1
  Q=0 and ~Q=1
S=1 and R=1
  Q=0 and ~Q=0
  ???

## Slide 10: Flip-flops
D-Latch
  Clock input C
  Data input D

## Slide 11: Operation of a D-Latch

## Slide 12: More on D-Latch
Q changes as D changes when clock is up
Not really edge-triggered
Notes: Want edge-triggered to make sure everything is synchronized

## Slide 13: Difference btw. Latch and Flip-flop
Latch
  Asynchronous
    Output changes soon after input changes
Flip-flop
  Synchronous
    Output changes at the clock edge
Notes: Output changes soon after input changes [when the clock is asserted (?)]

## Slide 14: D Flip Flop
D Flip Flop with a Falling-Edge Trigger

## Slide 15: Operation of D Flip Flop
D Flip Flop with a Falling Edge Trigger

## Slide 16: Setup Time and Hold Time
The input must be stable for a period of time before and after the clock edge
  Setup Time
    The minimum time the signal must be stable before clock edge
  Hold Time
    The minimum time the signal must be stable after clock edge
    Usually very small

## Slide 17: Register Files
A register file consists of a set of registers that can be read and written by supplying a register number
  Built from an array of D Flip-Flops
  A decoder is used to select a register in the register file

## Slide 18: Reading Registers
Multiplexor
  Select data from the specific register

## Slide 19: Writing to a register
Write Signal
  Specify a write operation to the register
Decoder
  Specify which register to write
Register Data
  Data to write to the register

## Slide 20: Register Files
Register Files
  Can be used to build small memory
  Too costly to build large amount of memory
Large Scale Memory
  Static random access memories (SRAM)
  Dynamic random access memories (DRAM)

## Slide 21: SRAMs
SRAM
  Integrated circuits of memory arrays
  A single access port
    Either read or write
    Fixed access time to any datum
  Height
    Number of addressable locations
  Width
    Number of output bits per unit
Example: 8Mx8 SRAM
  8M = 223, 23 address lines
  8 output bits

## Slide 22: 2Mx16 SRAM
21-bit address line
16-bit data input/output

## Slide 23: Implementation of Large SRAM
Register File
  Use Multiplexor
    32x1 Multiplexor
Large SRAM
  Impractical to use a large multiplexor like 64kx1
  Try to remember the implementation of a two input multiplexor
  Solution
    A more efficient implementation of Multiplexor
    Shared output line (bit line)
      Allow multiple sources to drive a single output line

## Slide 24: Small SRAM (4 x 2)

## Slide 25: Three State Buffer
  Two inputs
    A data signal
    An output enable (output select)
  A single output
    Three states
      Output enable = 1
        Asserted (1) state
        Deasserted (0) state
      Output enable = 0
        High Impedance state
        Allow the another three-state buffer with output enable =1 to determine the output

## Slide 26: Multiplexor using Three-State Buffers
Three-State Buffer
  Two inputs
    A data signal
    An output enable (output select)
  A single output
    Three states
      Output enable = 1
        Asserted (1) state
        Deasserted (0) state
      Output enable = 0
        High Impedance state
        Allow the another three-state buffer with output enable =1 to determine the output

## Slide 27: Organization of a 4M SRAM
Array of 8 Modules – Each for a bit
  Addr 21-10
    Use a 12 to 4096 decoder
    Select an array of1024 bits out of 4K 1024 bits
  Addr 9-0
    Select 1 bit from the 1024 bits as an output bit

## Slide 28: DRAM
SRAM
  Requires 4-6 transistors per bit
  Fast
  But costly
DRAM
  Requires 1 transistor per bit
  Charge stored in a capacitor
    Needs to be refreshed periodically
    Slower than SRAM
  But less expensive

## Slide 29: Organization of a 4M DRAM
  Addr 11-21
    Select 1 row from 2048 rows
  Addr 10-0
    Select 1 bit from the 2048 bits as an output bit
  Column Latches
    Store the selected output from 2048x2048 array temporally

## Slide 30: DRAM

## Slide 31: SRAM and DRAM
SRAM
  Fast but costly
  Small amount
  Used for Computer Cache
DRAM
  Slow but less costly
  Large amount
  Used for Computer Main Memory

## Slide 32: What I want you to do
Finish/Review Appendix B.1-3, B.5-B.9
Work on HW 2
Study for exam 1!