## Slide 1: Logic Design
Instructor: Robert Utterback
Lecture 4
Notes: In this lecture you’re going to learn a lot of new things: the basic building blocks of a computer. We’ll slowly combine these to learn how many components of a computer are built up.

## Slide 2: 0s and 1s
Modern Computers are Digital
1
  Corresponding to a high voltage
  Signal asserted
  Logical True
0
  Corresponding to low voltage
  Signal deasserted
  Logical False
0s and 1s are complimentary
  0’s inverse is 1
  1’s inverse is 0
Notes: Everything we’re going to do involves just these two values! Everything can be represented this way, and all the operations we need to do just combine 0s and 1s. This is also the reason we use the binary system to represent numbers….

## Slide 3: Binary Representation of Positive Integers
0 : 0000 0000
1 : 0000 0001
2 : 0000 0010
3 : 0000 0011
4 : 0000 0100
5 : 0000 0101
6 : 0000 0110
7 : 0000 1111
8 : 0000 1000
16: 0001 0000
32: 0010 0000
64: 0100 0000
128:1000 0000
Notes: Each of the columns represents a power of 2. Just like in decimal each column represents a power of 10. Example...

## Slide 4: Binary Representation of Positive Integers
100
100 = 64 + 32 + 4
0 1 1 0 0 1 0 0
Notes: Using a different numbering system has been done before – Babylonians used a base-60 system, Mayans used a base-20 system.

## Slide 5: Binary Representation of Positive Integers
45
45 = 32 + 8 + 4 + 1
0 0 1 0 1 1 0 1
Notes: So we can represent all our numbers in binary. And in fact we can represent everything we want in binary. AND we can perform any operations by just manipulating ones and zeros. We'll do it by building up blocks of logic functions.

## Slide 6: Combinational Logic and Sequential Logic
Combinational Logic
  A logic system without (changeable) memory
  Computes the same output given the same input
Sequential Logic
  A group of logic elements that contain memory
  Value depends on the inputs as well as the current contents of the memory
Notes: Logic: performs “logical” operations on boolean inputs. Everything we want to do can be built up from just a few logical operations…

## Slide 7: Boolean Logic -- AND
AND (Logical Product)
  Its output = 1, only if both inputs are 1
  Truth table
A | B | A·B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: We can actually do a special type of algebra: Boolean algebra (named after George Boole, a 19th century mathematician)

## Slide 8: Boolean Logic -- OR
OR (Logical Sum)
  Its output = 1 if either input = 1
  Truth table
A | B | A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 9: Boolean Logic -- NOT
NOT (Logical Inversion)
      or ~A
  The output is the opposite of the input
  Truth Table
A | ~A
0 | 1
1 | 0

## Slide 10: Order of Precedence
Precedence Rule
  Parentheses (Highest)
  NOT
  AND
  OR
Example
Notes: Having AND before OR fits with using multiplication symbol for AND and plus for OR. But if you ever forget this and/or just want to make it clear, just use parentheses! It’s never wrong. This goes for basically any situation where precedence might not be clear, especially while programming.

## Slide 11: Boolean Logic
Any Boolean Logic function can be implemented with only NOT, AND, OR functions
  NOT, AND, OR functions are the basic logic functions
  Others can be implemented by the basic logic functions NOT, AND, OR
Notes: Because a combinational logic block has no memory, we can specify it just by defining the values of the outputs for each set of input values.

## Slide 12: Truth Table
Example: A logic functions with three inputs, A, B, and C, and three outputs, D, E, and F.
  D is true if at most two inputs are true
  E is true if exactly two inputs are true
  F is true only if all three inputs are false
Notes: Because a combinational logic block has no memory, we can specify it just by defining the values of the outputs for each set of input values.

## Slide 13: Answer
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0

## Slide 14: Boolean Logic Laws
Identity Law
Zero and One Law
Inverse Law
Commutative Law
Notes: Notice that this is why we use + for OR and * for AND!

## Slide 15: Boolean Logic Laws (cont.)
Associative Laws
Distributive Laws
De Morgan’s Laws
Notes: Associative and distributive are as expected. DeMorgan’s laws are new to us.

## Slide 16: How to prove a logical law?
One approach: Truth table
Truth table for de Morgan Laws
Notes: Exercise: draw the truth table for deMorgan’s laws. Now that we've talked about the boolean logic functions we're using, we need to implement them...

## Slide 17: Gates
Gates
  basic digital building blocks which correspond to and perform the basic logical functions
AND
OR
NOT
Complex digital functions that make up a computer are built from these basic digital building blocks
Notes: Let's (together) design the block for implementing ~(~A + B)

## Slide 18: Simplification of NOT Gate

## Slide 19: Exercise
Design a Combinational Logic to implement the following logical expression
Y = (A + B) + C
Notes: Occasionally you’ll just see a bunch of wires coming into a gate, since the operations are associative and commutative.

## Slide 20: Exercise
Design a Combinational Logic to implement the following logical expression
Y = (A + B) · (C + A)

## Slide 21: NAND
NAND
  Its output = 1, only if both inputs are not 1
  Boolean Expression: A • B
  Truth Table
  The NAND functions has traditionally been the universal gate in digital circuits. It is simple to implement in hardware and can be used to construct the other gates.
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 22: NOR
NOR
  Its output = 1, only if no inputs are not 1
  Boolean Expression: A + B
  Truth Table
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 23: XOR
XOR is EXCLUSIVE-OR
  Its output = 1 if the inputs are different and equal 0 if all are the same. Boolean Expression: A Å B
  Truth Table
  Equivalent to (A•B) + (A•B) = C
A
C
B
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 24: Summary
0s and 1s in Computer
Binary
Boolean Logic
  NOT, AND, OR
  Boolean Logic Laws
Truth Table
Gates
  Basic Gates
    NOT, AND, OR
  Other Gates
    NAND, NOR, XOR