## Slide 1: Simple DataPath Implementation (4.4)
Lecture 37
Notes: Try to come up with as much of the data path diagram as we can

## Slide 2: Datapath With Control
Notes: We’ve implemented all but jump instructions…
What does a jump instruction look like (machine format)
And what does it need to do exactly?

## Slide 3: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump
Notes: Why the 00?
Let’s see if we can add this to our diagram

## Slide 4: Datapath With Jumps Added
Notes: Notice how EVERYTHING is happening in parallel, at the same time. For example, the 0-25 instruction bits get shifted and concatenated as if they were a jump address even when they were not. It’s the multiplexors that choose whether or not that value is actually used.

## Slide 5: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining
Notes: Notice CPI is 1 here, but clock period is long…
Before we go on, exercise:

## Slide 6: Exercise
New instruction: lwi rt, rd(rs)
Meaning:
  Reg[rt] = Mem[Reg[rd] + Reg[rs]]
How to implement this?
  What datapath blocks are used?
  What new blocks?
  What new control signals?

## Slide 7: Pipelining Overview
4.5
Notes: Walk me through the process of doing laundry.

## Slide 8: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/(0.5n + 1.5) ≈ 4 = number of stages
Notes: 0.5*4*n / (1.5 + 0.5n)
Not exactly 4 b/c of “startup”, pipeline is not full

## Slide 9: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 10: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 11: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Notes: What’s the speedup here?

## Slide 12: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
Notes: Time between instructions is really talking about the cycle time…

## Slide 13: Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle