## Slide 1: Logical Equations (B.2) & Combinational Logic (B.3)
Instructor: Robert Utterback
Lecture 5
Notes: In this lecture you’re going to learn a lot of new things: the basic building blocks of a computer. We’ll slowly combine these to learn how many components of a computer are built up.

## Slide 2: Review
57 in binary
What number is 1111 10112?

## Slide 3: Boolean Logic Laws
Identity Law
Zero and One Law
Inverse Law
Commutative Law
Notes: Notice that this is why we use + for OR and * for AND!

## Slide 4: Boolean Logic Laws (cont.)
Associative Laws
Distributive Laws
De Morgan’s Laws
Notes: Associative and distributive are as expected. DeMorgan’s laws are new to us.

## Slide 5: How to prove a logical law?
One approach: Truth table
Truth table for de Morgan Laws
Notes: Exercise: draw the truth table for deMorgan’s laws. Now that we've talked about the boolean logic functions we're using, we need to implement them...

## Slide 6: Gates
Gates
  basic digital building blocks which correspond to and perform the basic logical functions
AND
OR
NOT
Complex digital functions that make up a computer are built from these basic digital building blocks
Notes: Let's (together) design the block for implementing ~(~A + B)

## Slide 7: Simplification of NOT Gate

## Slide 8: Exercise
Design a Combinational Logic to implement the following logical expression
Y = (A + B) + C
Notes: Occasionally you’ll just see a bunch of wires coming into a gate, since the operations are associative and commutative.

## Slide 9: Exercise
Design a Combinational Logic to implement the following logical expression
Y = (A + B) · (C + A)

## Slide 10: NAND
NAND
  Its output = 1, only if both inputs are not 1
  Boolean Expression: A • B
  Truth Table
  The NAND functions has traditionally been the universal gate in digital circuits. It is simple to implement in hardware and can be used to construct the other gates.
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 11: NOR
NOR
  Its output = 1, only if no inputs are not 1
  Boolean Expression: A + B
  Truth Table
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 12: XOR
XOR is EXCLUSIVE-OR
  Its output = 1 if the inputs are different and equal 0 if all are the same. Boolean Expression: A Å B
  Truth Table
  Equivalent to (A•B) + (A•B) = C
A
C
B
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 13: Summary
0s and 1s in Computer
Binary
Boolean Logic
  NOT, AND, OR
  Boolean Logic Laws
Truth Table
Gates
  Basic Gates
    NOT, AND, OR
  Other Gates
    NAND, NOR, XOR

## Slide 14: Exercise
Show how to build AND, OR, and NOT functions from (two-input) NAND gates.
Notes: Start of B.3
Let Nand = @
~A = A @ A
AND = ~(A @ B) = (A @ B) @ (A @ B)
OR = ~A @ ~B = (A @ A) @ (B @ B)

## Slide 15: Decoder
Decoder
  A logic block that has n-bit input and 2n outputs, where only one output is asserted for each input combination
  If the input is i (in binary),
    then output i is 1
    others are 0
Notes: N bit input -> 2^N permutations. You’ll see this relationship everywhere, so I want to make it a little clearer for you. 2 choices for the first bit, 2 for the second, etc.

## Slide 16: Decoder Example
3-8 Decoder
Notes: There’s also such thing as an “encoder” to go in the other direction: n separate choices to a log_n bit number.
We’ll see in just a second an example of why you might need a decoder.

## Slide 17: Multiplexor
Multiplexor
  A selector
    The output is selected by an input control

## Slide 18: Implementation of a Multiplexor

## Slide 19: n-input Multiplexor
A Multiplexor can have n-inputs
  Require selective inputs
Implementation of an n-input Multiplexor
  Decoder generates n signals. Each indicates different input value.
  Array of n AND gates. Each combines one input with decoder signal
  3. Single large OR gate taking all outputs of AND gates.
Notes: To have n inputs, log n is enough, since we only need to select one at a time. x bits gives us 2^x permutations, hence log n gives us a way to select one input from n.

## Slide 20: Two-level Logic
Remember: Any Boolean Logic function can be implemented with only NOT, AND, OR functions
We can also find that all logic functions can be written in a canonical form
  Sum of Products
    Logical Sum (OR) of terms joined by Product (AND)
  Product of Sums
    Logical Product (AND) of terms joined by Sum (OR)
Notes: In fact, we can say something even stronger. The textbook uses Sum of Products.
Why? B/c It’s really easy to figure out from a truth table. For every 1 you see, just add another product!

## Slide 21: Example
Consider the following:
  C)+(B C)) (
Convert to sum of products form
  B
Notes: Hint: draw a truth table. When the final result is one, just add another product group to the sum.