## Slide 1: Pipelining Overview
4.5
Notes: Walk me through the process of doing laundry.

## Slide 2: Datapath With Jumps Added
Notes: Notice how EVERYTHING is happening in parallel, at the same time. For example, the 0-25 instruction bits get shifted and concatenated as if they were a jump address even when they were not. It’s the multiplexors that choose whether or not that value is actually used.

## Slide 3: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 4: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/(0.5n + 1.5) ≈ 4 = number of stages
Notes: 0.5*4*n / (1.5 + 0.5n)
Not exactly 4 b/c of “startup”, pipeline is not full

## Slide 5: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 6: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
Notes: Clock cycle must be 800ps in single-cycle processor.

## Slide 7: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Notes: Q: What’s actual speedup? A: 2400/1400
Q: After we “warmup” the pipeline, each lw finishes in 200 ps. Each in the single-cycle takes 800ps.
So if we have a lot of instructions (say, 1M), the speedup is approximately what? A: ~2400/200 = 12

## Slide 8: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
Notes: Time between instructions is really talking about the cycle time…
Can evenly split cycle time if all steps are balanced

## Slide 9: Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 10: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 11: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
Notes: Laundry: a combination washer and dryer
Also: FP units

## Slide 12: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 13: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath
Notes: Result of add is actually read ahead of time! Just twiddling thumbs during mem stage, then writing it back.
How about a shortcut?
Also extra control signals to decide when to use that value!

## Slide 14: Forwarding
Notes: Draw ALU -> ALU forwarding loop.
Makes control a bit harder…doesn’t just depend on instruction now, can depend on instructions surrounding!

## Slide 15: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 16: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles
Notes: Example on page 280
Q: Left: What are the stalls? How many cycles total?
Q: How could you rearrange to do better?
Q: How many stalls/cycles?