## Slide 1: Pipelining IMPLEMENTATION
4.6
Notes: Q: What was our analogy for pipelining? Give me a high-level overview of pipelining

## Slide 2: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/(0.5n + 1.5) ≈ 4 = number of stages
Notes: Q: What’s a hazard? What types of hazards did we have?

## Slide 3
Which of the statements below is true about a pipelined processor?
Selection | Statement
A | Instruction latency remains essentially unchanged from single-cycle (minus some overheads); Instruction throughput increases
B | Instruction latency decreases; Instruction throughput increases
C | Instruction latency remains essentially unchanged (minus some overheads); Instruction throughput decreases
D | Instruction latency improves (decreases); Instruction throughput increases
E | None of the above
Pipelining Performance
Notes: Correct Answer – A
Also better utilization

## Slide 4
Should we force every instruction to go through all 5 stages? Can we break it up so that R-type takes only 4 cycles instead of 5? Skip the Mem. Stage and WB immediately after ALU.
Selection | Yes/No | Reason (Choose BEST answer)
A | Yes | Decreasing R-type to 4 cycles improves instruction throughput
B | Yes | Decreasing R-type to 4 cycles improves instruction latency
C | No | Decreasing R-type to 4 cycles causes hazards
D | No | Decreasing R-type to 4 cycles causes hazards and doesn’t impact throughput
E | No | Decreasing R-type to 4 cycles causes hazards and doesn’t impact latency
Pipeline Stages
Notes: Tails - flipped
Correct Answer - C

## Slide 5: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 6: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
Notes: Laundry: a combination washer and dryer
Also: FP units

## Slide 7: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 8: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath
Notes: Result of add is actually read ahead of time! Just twiddling thumbs during mem stage, then writing it back.
How about a shortcut?
Also extra control signals to decide when to use that value!

## Slide 9: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 10: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles
Notes: Example on page 280
Q: Left: What are the stalls? How many cycles total?
Q: How could you rearrange to do better?
Q: How many stalls/cycles?

## Slide 11: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage
Notes: So first, branch uses relative addressing, so we need to add. But the result of the add won’t be ready until later in the pipeline, even though we need it immediately.

## Slide 12: Stall on Branch
Wait until branch outcome determined before fetching next instruction
Notes: Even when we add hardware to compute the address in the ID stage (Reg), we still have to stall!

## Slide 13: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay
Notes: Modern chips often split their pipeline into more stages (30+).

## Slide 14: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect
Notes: Actually lots of details here, may need to “undo” things.

## Slide 15: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history
Notes: This kind of speculation is great for performance…
…but also led to the recent Spectre and Meltdown security exploits!

## Slide 16: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture
Notes: Examples on p. 285
Stall on lw result
Bypass the first add result written into $t1
No stall or bypass required.