## Slide 1: Measuring Performance II and Logic Design
Instructor: Robert Utterback
Lecture 3

## Slide 2: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture
Notes: Note that CPI differs for different instructions, so we need the average for a particular set of instructions.
In this course we will assume the clock period is fixed, but I should note that in modern CPUs this is not necessarily the case. Recent CPUs will actually lower their clock speed when the machine isn't busy to save energy.

## Slide 3: Review
 | P1 | P2 | P3
Clock rate | 3 GHz | 2.5 GHz | 4.0 GHz
CPI | 1.5 | 1.0 | 2.2
Three processors, same ISA:
Each executes a program in 10s.
  How many cycles?
  How many instructions?

## Slide 4: SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)
Notes: Section 1.9
In general, for units that are proportional to time (like latency or response time), use arithmetic mean.
For unitless quantities (e.g. speedup ratios) use the geometric mean

## Slide 5: CINT2006 for Intel Core i7 920
Notes: Notice the high CPI values in some of the benchmarks. This is typically because of high cache miss rates.

## Slide 6: SPEC Power Benchmark
Power consumption of server at different workload levels
  Performance: ssj_ops/sec
  Power: Watts (Joules/sec)

## Slide 7: SPECpower_ssj2008 for Xeon X5650

## Slide 8: Fallacy: Low Power at Idle
Look back at i7 power benchmark
  At 100% load: 258W
  At 50% load: 170W (66%)
  At 10% load: 121W (47%)
Google data center
  Mostly operates at 10% – 50% load
  At 100% load less than 1% of the time
Consider designing processors to make power proportional to load

## Slide 9: Pitfall: MIPS as a Performance Metric
MIPS: Millions of Instructions Per Second
  Doesn’t account for
    Differences in ISAs between computers
    Differences in complexity between instructions
  CPI varies between programs on a given CPU
Notes: Big picture: execution time is the only measure of performance that is always valid. Sometimes other metrics are valid in a limited context, but it is an error to use them beyond that context.

## Slide 10: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.10 Fallacies and Pitfalls
Notes: Section 1.10
A pitfall to expect that performance improvement, but Amdahl's law itself is actually a really useful tool.

## Slide 11: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.10 Fallacies and Pitfalls
Example: A program runs for 100 s. 80 s are due to multiplication instructions.
  How much do we need to improve the multiply to achieve 2x performance?
Notes: Section 1.10
Example: a program runs 100 s, with multiply operations accounting for 80 s of the time
Basically law of diminishing returns

## Slide 12: Amdahl’s Law
Example: A program runs for 100 seconds. Of the 100 seconds, 80 seconds are due to multiplies.
  2x improvement: n = 2.66
  3x improvement: n = 6
  4x improvement: n = 16
  5x improvement: n = ?
Corollary: make the common case fast
  Can’t be done!
Notes: Also used for calculating how much improvement you can get when writing a parallel program.

## Slide 13: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance
§1.9 Concluding Remarks
Notes: Section 1.11

## Slide 14: What I want you to do
Finish Chapter 1
Read Appendix B.1-B.3
Work on homework 1