## Slide 1: The Memory Hierarchy
Chapter 5
Notes: On a write hit, one thing we could do it always write the result back to memory. What is this called (write-through)
What’s the alternative? (write-back, which only writes back to memory when a block is kicked out of memory)
It’s a waste to write back to memory if we haven’t changed the block since it came into cache. How do we handle this? (dirty bit)

## Slide 2: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:
§5.4 Measuring and Improving Cache Performance
Notes: Now let’s dig a little deeper into cache performance.
In particular, we assume that our write buffer never gets too full, or if it does it’s too infrequent to matter.

## Slide 3: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)
Notes: Fully associative is actually the scheme Abhi suggested, though it’s faster than I implied, since we can do all the searches in parallel.

## Slide 4: Associative Cache Example

## Slide 5: Spectrum of Associativity
For a cache with 8 entries

## Slide 6: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 |  |  |  |  |  | 
8 |  |  |  |  |  | 
0 |  |  |  |  |  | 
6 |  |  |  |  |  | 
8 |  |  |  |  |  | 
Notes: What does it look like (contents, misses)
| Block address | Cache index | Hit/miss | 0 | 1 | 2 | 3 |
|---------------+-------------+----------+--------+---+--------+---|
| 0 | 0 | miss | Mem[0] | | | |
| 8 | 0 | miss | Mem[8] | | | |
| 0 | 0 | miss | Mem[0] | | | |
| 6 | 2 | miss | Mem[0] | | Mem[6] | |
| 8 | 0 | miss | Mem[8] | | Mem[6] | |

## Slide 7: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 8: Associativity Example
2-way set associative
Fully associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
0 |  |  |  |  |  | 
8 |  |  |  |  |  | 
0 |  |  |  |  |  | 
6 |  |  |  |  |  | 
8 |  |  |  |  |  | 
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 |  |  |  |  |  | 
8 |  |  |  |  |  | 
0 |  |  |  |  |  | 
6 |  |  |  |  |  | 
8 |  |  |  |  |  | 
Notes: Now what do these look like? In particular, how many misses?
| Block address | Cache index | Hit/miss | 0 | 1 | 2 | 3 |
|---------------+-------------+----------+--------+--------+---+---|
| 0 | 0 | miss | Mem[0] | | | |
| 8 | 0 | miss | Mem[0] | Mem[8] | | |
| 0 | 0 | hit | Mem[0] | Mem[8] | | |
| 6 | 0 | miss | Mem[0] | Mem[6] | | |
| 8 | 0 | miss | Mem[8] | Mem[6] | | |
| Block address | Cache index | Hit/miss | 0 | 1 | 2 | 3 |
|---------------+-------------+----------+--------+--------+--------+---|
| 0 | | miss | Mem[0] | | | |
| 8 | | miss | Mem[0] | Mem[8] | | |
| 0 | | hit | Mem[0] | Mem[8] | | |
| 6 | | miss | Mem[0] | Mem[8] | Mem[6] | |
| 8 | | hit | Mem[0] | Mem[8] | Mem[6] | |

## Slide 9: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 10: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%