## Slide 1: The Memory Hierarchy
Chapter 5
Notes: On a write hit, one thing we could do it always write the result back to memory. What is this called (write-through)
What’s the alternative? (write-back, which only writes back to memory when a block is kicked out of memory)
It’s a waste to write back to memory if we haven’t changed the block since it came into cache. How do we handle this? (dirty bit)

## Slide 2: Associative Cache Example

## Slide 3: Spectrum of Associativity
For a cache with 8 entries

## Slide 4: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 5: Set Associative Cache Organization
Notes: But as soon as we allow multiple ways, we have a new choice to make.
When we need to kick something out of cache, which way do we choose?

## Slide 6: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 7: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L2 cache misses
Some high-end systems include L3 cache

## Slide 8: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache, effective CPI?
Notes: Calculate the effective CPI with just a primary cache…
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 9: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 10: Example (cont.)
Now add L2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L2 hit
  Penalty = ???
Notes:   Penalty (in cycles?)
  5ns/0.25ns = 20 cycles

## Slide 11: Example (cont.)
Now add L2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L2 miss
  Extra penalty = ???
Notes: Extra penalty in cycles?
  100ns/0.25ns = 400 cycles

## Slide 12: Example (cont.)
Now add L2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L2 miss
  Extra penalty = 100ns/0.25ns = 400 cycles
CPI = ???
Notes: 1 + 0.02 × 20 + 0.005 × 400 = 3.4

## Slide 13: Example (cont.)
Now add L2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L2 miss
  Extra penalty = 100ns/0.25ns = 400 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6
Notes: Notice you could have calculated this a different way, too….

## Slide 14: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L1 cache usually smaller than a single cache
  L1 block size smaller than L2 block size
Notes: The l2 (or l3) is kind of like your last-ditch/resort effort

## Slide 15: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation

## Slide 16: Interactions with Software
Misses depend on memory access patterns
Algorithm behavior
Compiler optimization for memory access
Hardware prefetch

## Slide 17: Software Optimization via Blocking
Goal: maximize accesses to data before it is replaced
Consider inner loops of DGEMM:
for (int j = 0; j < n; ++j)
{
double cij = C[i+j*n];
for( int k = 0; k < n; k++ )
cij += A[i+k*n] * B[k+j*n];
C[i+j*n] = cij;
}

## Slide 18: DGEMM Access Pattern
C, A, and B arrays
older accesses
new accesses

## Slide 19: Cache Blocked DGEMM
1 #define BLOCKSIZE 32
2 void do_block (int n, int si, int sj, int sk, double *A, double
3 *B, double *C)
4 {
5 for (int i = si; i < si+BLOCKSIZE; ++i)
6 for (int j = sj; j < sj+BLOCKSIZE; ++j)
7 {
8 double cij = C[i+j*n];/* cij = C[i][j] */
9 for( int k = sk; k < sk+BLOCKSIZE; k++ )
10 cij += A[i+k*n] * B[k+j*n];/* cij+=A[i][k]*B[k][j] */
11 C[i+j*n] = cij;/* C[i][j] = cij */
12 }
13 }
14 void dgemm (int n, double* A, double* B, double* C)
15 {
16 for ( int sj = 0; sj < n; sj += BLOCKSIZE )
17 for ( int si = 0; si < n; si += BLOCKSIZE )
18 for ( int sk = 0; sk < n; sk += BLOCKSIZE )
19 do_block(n, si, sj, sk, A, B, C);
20 }

## Slide 20: Blocked DGEMM Access Pattern
Unoptimized
Blocked

## Slide 21: Dependability
Fault: failure of a component
  May or may not lead to system failure
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration
§5.5 Dependable Memory Hierarchy

## Slide 22: Dependability Measures
Reliability: mean time to failure (MTTF)
Service interruption: mean time to repair (MTTR)
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair
Notes: These terms are often thrown around vaguely, but we have actual definitions for them.

## Slide 23: The Hamming SEC Code
Hamming distance
  Number of bits that are different between two bit patterns
Minimum distance = 2 provides single bit error detection
  E.g. parity code
Minimum distance = 3 provides single error correction, 2 bit error detection