## Slide 1: SubWord Parallelism for matrix multiply
Instructor: Robert Utterback
Lecture 31
Notes: Q: What’s a guard bit? What about sticky bit?

## Slide 2: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes (round to nearest even)
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements
Notes: Guard = first extra bit, round = second extra bit
3 significant bits (counting the digit before decimal point), just a base 10 example for simplicity
Ex: 2.56 x 10^0 + 2.34 x 10^2, with and without guard and round (p. 219) (do without FIRST)
Now explain rounding modes, THEN sticky bit
Another Ex: 5.01 x 10^-1, 2.34 x 10^2
Yields 0.0050 + 2.34 = 2.3450, need to set the sticky bit
Use sticky bit to round, since we often round to the nearest even
What if we had 5.01 x 10^-42? Then that .01 part would be shifted VERY far over. But we don’t need to store all those bits, just the sticky “flag”

## Slide 3: FP Example: Matrix Multiplication
X = X + Y × Z
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double x[32][32], double y[32][32], double z[32][32]) { for (int i = 0; i != 32; i++) for (int j = 0; j != 32; j++) for (int k = 0; k != 32; k++) x[i][j] = x[i][j] + y[i][k] * z[k][j]; }
  Addresses of x, y, z in $a0, $a1, $a2, and i, j, k in $s0, $s1, $s2
Notes: Explain basic idea behind a matrix; they will see it a lot in Linear Algebra. Used in all kinds of places, e.g., computer graphics, scientific calculations, machine learning, etc.
Declaring double x[32][32] is really just declaring a 32*32 size array, but let’s you use the double brackets to index.
Actual index calculation for, e.g., x[i][j] is tricky
Need the ith row and jth column.
First need to figure out which “slot” we’re in: i * size of row = i * 32, then add column number (j)
Then: how big is each slot? 8 bytes, so take that value * 8, then add to start of array. Whew!
That’s the actual byte address we need to load.
Q: (Exercise): calculate the byte address of x[i][j]

## Slide 4: Example: Matrix Multiplication
MIPS code:
li $t1, 32 # $t1 = 32 (row size/loop end) li $s0, 0 # i = 0; initialize 1st for loop L1: li $s1, 0 # j = 0; restart 2nd for loop L2: li $s2, 0 # k = 0; restart 3rd for loop sll $t2, $s0, 5 # $t2 = i * 32 (size of row of x) addu $t2, $t2, $s1 # $t2 = i * size(row) + j sll $t2, $t2, 3 # $t2 = byte offset of [i][j] addu $t2, $a0, $t2 # $t2 = byte address of x[i][j] l.d $f4, 0($t2) # $f4 = 8 bytes of x[i][j] L3: sll $t0, $s2, 5 # $t0 = k * 32 (size of row of z) addu $t0, $t0, $s1 # $t0 = k * size(row) + j sll $t0, $t0, 3 # $t0 = byte offset of [k][j] addu $t0, $a2, $t0 # $t0 = byte address of z[k][j] l.d $f16, 0($t0) # $f16 = 8 bytes of z[k][j] …
Notes: Note the complicated index calculation. First we calculate which element of the matrix we need by looking at row and column. Kind of like “flattening” the 2D matrix into one dimensional memory. THEN we use the size of each element (sll by 3) to calculate actual byte offset, then add to base to get byte address.

## Slide 5: Example: Matrix Multiplication
… sll $t0, $s0, 5 # $t0 = i*32 (size of row of y) addu $t0, $t0, $s2 # $t0 = i*size(row) + k sll $t0, $t0, 3 # $t0 = byte offset of [i][k] addu $t0, $a1, $t0 # $t0 = byte address of y[i][k] l.d $f18, 0($t0) # $f18 = 8 bytes of y[i][k] mul.d $f16, $f18, $f16 # $f16 = y[i][k] * z[k][j] add.d $f4, $f4, $f16 # f4=x[i][j] + y[i][k]*z[k][j] addiu $s2, $s2, 1 # $k k + 1 bne $s2, $t1, L3 # if (k != 32) go to L3 s.d $f4, 0($t2) # x[i][j] = $f4 addiu $s1, $s1, 1 # $j = j + 1 bne $s1, $t1, L2 # if (j != 32) go to L2 addiu $s0, $s0, 1 # $i = i + 1 bne $s0, $t1, L1 # if (i != 32) go to L1
Notes: The book for some reason loves to put their termination condition checks at the end, though to me it’s more intuitive to do it at the beginning…
Q: What’s the problem with putting it at the end?
A: If you’re not 100% sure the termination condition will be satisfied the first iteration, this code executes 1 iteration when it should execute 0!
But this is an optimization (skips one check), if you know for sure that your loop will run one iteration.

## Slide 6: Subword Parallellism
Graphics and audio applications can take advantage of performing simultaneous operations on short vectors
  Example: 128-bit adder:
    Sixteen 8-bit adds
    Eight 16-bit adds
    Four 32-bit adds
Also called data-level parallelism, vector parallelism, or Single Instruction, Multiple Data (SIMD)
§3.6 Parallelism and Computer Arithmetic: Subword Parallelism
Notes: Newer MIPS extensions actually have some SIMD instructions, but we’ll just look at the x86 versions.

## Slide 7: x86 FP Architecture
Originally based on 8087 FP coprocessor
  8 × 80-bit extended-precision registers
  Used as a push-down stack
  Registers indexed from TOS: ST(0), ST(1), …
FP values are 32-bit or 64 in memory
  Converted on load/store of memory operand
  Integer operands can also be converted on load/store
Very difficult to generate and optimize code
  Result: poor FP performance
§3.7 Real Stuff: Streaming SIMD Extensions and AVX in x86

## Slide 8: x86 FP Instructions
Optional variations
  I: integer operand
  P: pop operand from stack
  R: reverse operand order
  But not all combinations allowed
Data transfer | Arithmetic | Compare | Transcendental
FILD mem/ST(i) FISTP mem/ST(i) FLDPI FLD1 FLDZ | FIADDP mem/ST(i) FISUBRP mem/ST(i) FIMULP mem/ST(i) FIDIVRP mem/ST(i) FSQRT FABS FRNDINT | FICOMP FIUCOMP FSTSW AX/mem | FPATAN F2XMI FCOS FPTAN FPREM FPSIN FYL2X

## Slide 9: Streaming SIMD Extension 2 (SSE2)
Adds 4 × 128-bit registers
  Extended to 8 registers in AMD64/EM64T
Can be used for multiple FP operands
  2 × 64-bit double precision
  4 × 32-bit double precision
  Instructions operate on them simultaneously
    Single-Instruction Multiple-Data
Notes: If you have a 128-bit adder, it’s fairly easy to split it up to do 2 64 bit adds or 4 32 bit adds, so that’s what people did.
Newer versions have 256-bit registers (ymm) and even 512 bit registers (zmm)

## Slide 10: Matrix Multiply
Unoptimized code:
1. void dgemm (int n, double* A, double* B, double* C)
2. {
3. for (int i = 0; i < n; ++i)
4. for (int j = 0; j < n; ++j)
5. {
6. double cij = C[i+j*n]; /* cij = C[i][j] */
7. for(int k = 0; k < n; k++ )
8. cij += A[i+k*n] * B[k+j*n]; /* cij += A[i][k]*B[k][j] */
9. C[i+j*n] = cij; /* C[i][j] = cij */
10. }
11. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Notes: Original book code, very confusing

## Slide 11: Matrix Multiply
Unoptimized code:
1. void dgemm(int n, double* A, double* B, double* C)
2. {
3. for (int i = 0; i < n; ++i) // row
4. for (int j = 0; j < n; ++j) { // column
5. double cij = C[i*n+j]; /* cij = C[i][j] */
6. for(int k = 0; k < n; k++ ) // col of A, row of B
7. cij += A[i*n+k] * B[k*n+j]; /* cij += A[i][k]*B[k][j] */
8. C[i*n+j] = cij; /* C[i][j] = cij */
9. }
10. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Notes: This code is a little bit different and harder. If you don’t know the size of the matrix at compile time (before it was fixed at 32), then you have to do the array calculation manually, can’t just use C[i][j], e.g..
So this code is going the same thing it’s just a little harder to understand.
DGEMM = Double precision General Matrix Multiply

## Slide 12: Matrix Multiply
x86 assembly code:
1. vmovsd (%r10),%xmm0 # Load 1 element of C into %xmm0
2. mov %rsi,%rcx # register %rcx = %rsi
3. xor %eax,%eax # register %eax = 0
4. vmovsd (%rcx),%xmm1 # Load 1 element of B into %xmm1
5. add %r9,%rcx # register %rcx = %rcx + %r9
6. vmulsd (%r8,%rax,8),%xmm1,%xmm1 # Multiply %xmm1, element of A
7. add $0x1,%rax # register %rax = %rax + 1
8. cmp %eax,%edi # compare %eax to %edi
9. vaddsd %xmm1,%xmm0,%xmm0 # Add %xmm1, %xmm0
10. jg 30 <dgemm+0x30> # jump if %eax > %edi
11. add $0x1,%r11d # register %r11 = %r11 + 1
12. vmovsd %xmm0,(%r10) # Store %xmm0 into C element
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Notes: Notice opposite order of registers!
Working with just 64 bits of data, so don’t actually need “v” prefix, but used so that we can use the three-register versions of the instructions, e.g., vaddsd
Vmovsd = vector move scalar (single) double

## Slide 13: Matrix Multiply
Optimized C code:
1. #include <x86intrin.h>
2. void dgemm (int n, double* A, double* B, double* C)
3. {
4. for ( int i = 0; i < n; i+=4 )
5. for ( int j = 0; j < n; j++ ) {
6. __m256d c0 = _mm256_load_pd(C+i+j*n); /* c0 = C[i][j] */
7. for( int k = 0; k < n; k++ )
8. c0 = _mm256_add_pd(c0, /* c0 += A[i][k]*B[k][j] */
9. _mm256_mul_pd(_mm256_load_pd(A+i+k*n),
10. _mm256_broadcast_sd(B+k+j*n)));
11. _mm256_store_pd(C+i+j*n, c0); /* C[i][j] = c0 */
12. }
13. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Notes: Do groups of 4 at a time now…
But this code is incorrect! It is trying to load from 4 different rows of A at the same time, but the elements it wants are not contiguous!

## Slide 14: Matrix Multiply
Optimized C code:
1. #include <x86intrin.h>
2. void dgemm (int n, double* A, double* B, double* C)
3. {
4. for ( int i = 0; i < n; i++ ) // row
5. for ( int j = 0; j < n; j+=4 ) { // col
6. __m256d c0 = _mm256_load_pd(C+i*n+j); // c0 = C[i][j]
7. for( int k = 0; k < n; k++ )
8. c0 = _mm256_add_pd(c0, // c0 += A[i][k]*B[k][j]
9. _mm256_mul_pd(_mm256_broadcast_sd(A+i*n+k),
_mm256_load_pd(B+k*n+j)));
10. _mm256_store_pd(C+i*n+j, c0); /* C[i][j] = c0 */
11. }
12. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Notes: Do groups of 4 at a time now…take four columns of B at a time. Assume matrix size is multiple of 4…
The book does it just a little bit differently, but I think this is more intuitive.

## Slide 15: Matrix Multiply
Optimized x86 assembly code:
1. vmovapd (%r11),%ymm0 # Load 4 elements of C into %ymm0
2. mov %rbx,%rcx # register %rcx = %rbx
3. xor %eax,%eax # register %eax = 0
4. vbroadcastsd (%rax,%r8,1),%ymm1 # Make 4 copies of B element
5. add $0x8,%rax # register %rax = %rax + 8
6. vmulpd (%rcx),%ymm1,%ymm1 # Parallel mul %ymm1,4 A elements
7. add %r9,%rcx # register %rcx = %rcx + %r9
8. cmp %r10,%rax # compare %r10 to %rax
9. vaddpd %ymm1,%ymm0,%ymm0 # Parallel add %ymm1, %ymm0
10. jne 50 <dgemm+0x50> # jump if not %r10 != %rax
11. add $0x1,%esi # register % esi = % esi + 1
12. vmovapd %ymm0,(%r11) # Store %ymm0 into 4 C elements
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Notes: Vmovapd = vector move aligned packed double
Ymm registers are actually 256 bits! 4 doubles!

## Slide 16: Right Shift and Division
Left shift by i places multiplies an integer by 2i
Right shift divides by 2i?
  Only for unsigned integers
For signed integers
  Arithmetic right shift: replicate the sign bit
  e.g., –5 / 4
    111110112 >> 2 = 111111102 = –2
    Rounds toward –∞
  c.f. 111110112 >>> 2 = 001111102 = +62
§3.9 Fallacies and Pitfalls

## Slide 17: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 18: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles
Esoteric features, e.g. infinity, NaN
  Provide safe defaults
  Otherwise programmers would have to deal with all FP complexity

## Slide 19: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
§3.9 Concluding Remarks