## Slide 1: Measuring and discussing Performance
Instructor: Robert Utterback
Lecture 2

## Slide 2: Review
What are the steps to transform a program written in C into a representation that is directly executed by a computer processor?
Notes: Compile to assembly -> Assemble to machine code -> (link)

## Slide 3: An Analogy
Which airplane is the best?

## Slide 4: An Analogy
Which airplane is the best?

## Slide 5: Defining Performance
Which airplane has the best performance?
§1.6 Performance
Notes: Section 1.6

## Slide 6: Answer
That depends on …
  If performance means
    “the least time of transferring 1 passenger from one place to another”
      Concorde
    “the least time of transferring 450 passenger from one place to another”
      Boeing 747
Performance can be defined in different ways

## Slide 7: Measures of Performance
Execution Time
Throughput (ops/time)
Responsiveness
Performance / Cost
Performance / Power
Frame Rate

## Slide 8: Match Metric to Domain
Network bandwith (data/sec)
Network Latency (ms)
Frame Rate (frames/sec)
Throughput (ops/sec)
Selection | Online WoW | Crysis (FPS) | Torrent Download | Data Center
A | 4 | 3 | 1 | 2
B | 4 | 1 | 3 | 2
C | 2 | 1 | 3 | 4
D | 2 | 3 | 1 | 4
E | None of the above |  |  | 
Notes: D
Car example: they want something flashy, parents want something safe with room for trips.
Slide comes from Leo Porter’s materials.

## Slide 9: Response Time and Throughput
Response time (AKA Execution Time)
  How long it takes to do a task
Throughput (AKA Bandwith)
  Total work done per unit time
    e.g., tasks/transactions/… per hour
We’ll focus on response time for now…

## Slide 10: Response Time and Throughput
Selection | Response Time | Throughput
A | Increase | Increase
B | Decrease | Increase
C | Increase | Decrease
D | Decrease | Decrease
E | Same | Increase
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
Notes: Assume no change to the program.
Faster processor: reduces response time AND increases throughput = B
More processors: Increase throughput, same response time (probably, unless there is a backlog of tasks) = E
If you change your program to take advantage of the processors, however (or if your program automatically adapts…), the response time might decrease, so B again.

## Slide 11: Performance and Execution Time
Performance

## Slide 12: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B
Notes: SQ: How much faster is A than B?
Now let’s flip that on its head…

## Slide 13: Class Exercise
Computer B runs a program in 24 seconds.
Computer A runs the program 1.2 times faster.
How long does the program take on computer A?
Notes: Perf_A / Perf_B = 1.2 = Time_B / Time_A
=> Time_A = Time_B / 1.2 = 24 * 5/6 = 20 s

## Slide 14: Measuring Execution Time
Elapsed (Wallclock) time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
    User CPU time: CPU time spent in a program itself
    System CPU time: CPU time spent in the OS performing task on behalf of the program
  Different programs are affected differently by CPU and system performance
Notes: When we talk about elapsed time for a single program, we typically mean total response time on an unloaded machine.
We’ll really just talk about user CPU time.
Now let’s dig a little deeper into what things make up CPU time.

## Slide 15: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 16: CPU Time

## Slide 17: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
Hardware designer must often trade off clock rate against cycle count
Notes: Increasing clock rate
=> shorter clock period
=> Shorter instructions, but more of them
=> More total clock cycles
Reduce number of clock cycles
=> Fewer instructions,
but they become longer since they must be more complicated
=> longer clock period
=> reduced clock rate

## Slide 18: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?
Notes: 1 GHz = 10^9 cycles/sec
CPU Time = Clock cycles / Clock Rate
6s = exec time = clock cycles * clock period = clock cycles/clock rate = 1.2*old clock cycles / x
10s = old clock cycles / 2 GHz => old clock cycles = 10 * 2 * 10^9

## Slide 19: Instruction Set Architecture
Instruction Set Architecture (ISA)
  Abstract interface between HW and SW
  Encompasses all info needed to write a machine language program that will run correctly
    instructions
    Registers
    Memory access
    I/O
Notes: To go deeper we need details about the ISA

## Slide 20: Instruction Set Architecture
I/O system
Instr. Set Proc.
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture