## Slide 1: Instructions: Language of the Computer (Ch 2)
Instructor: Robert Utterback
Lecture 14
Notes: What did we talk about last time?
I-format, what’s that? What instructions do we know are I-format?

## Slide 2: Mini Green Sheet
MIPS instructions
  R:
  I:
Register numbers
  $t0 – $t7 : 8 – 15, $t8 – $t9 : 24 – 25
  $s0 – $s7 : 16 – 23, $zero : 0
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Notes: With a single exception, when op=0 it’s in R format

## Slide 3: Convert into MIPS Assembly
ae51 0000
1010 1110 0101 0001 0000 0000 0000 0000
101011 10010 10001 0…
43 18 17 0
sw $s1, 0($s2)

## Slide 4: In Class Exercise
Convert the following MIPS instructions into Machine Instructions (hex)
lw $t0, 200($s0)
Notes: 35 16 8 200
100011 10000 01000 00000000 11000100
1000 1110 0000 1000 0000 0000 1100 0100
8e0800c4

## Slide 5: Logical and Conditional Instructions
Instructor: Robert Utterback

## Slide 6: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture
Notes: The binary compatibility also requires same OS, libraries… but can use different chip that is same ISA.

## Slide 7: Logical Operations (2.6)
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations
Notes: ^ in C does bitwise XOR, which produces subtle bugs if you think it does exponentiation.

## Slide 8: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: We sometimes use this to get different bytes from a word.
Compare to base 10, multiplying by 10

## Slide 9: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 10: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 11: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 12: Making Decisions (2.7)

## Slide 13: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 14: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …
Assembler calculates addresses
Notes: The book seems to oversimply and say bne will be used. There are actually lots of factors here, and compilers try to decide which branch will be used more frequently and put that one right after the branch.

## Slide 15: Compiling Loop Statements
C code:
while (i != n) i += 1;
  i in $s3, nin $s5
Compiled MIPS code:
Loop: bne $s3, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …
Notes: Need to pause to explain while loops for those who haven’t had 161…start with a simpler while loop.

## Slide 16: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …
Notes: Note the addressing here: we don’t know the actual slot of the array ahead of time, so we have to do the multiplication first, then add, then use lw with 0(reg).

## Slide 17: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 18: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 19: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise
Notes: Q: How to do >? What about <=?
A: slt (<), beq else, beq else

## Slide 20: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 21: Exercise
C code:
if (x < y)
x--;
What does the MIPS assembly look like?
  x in $s0, y in $s1
Notes: Slt $t0, $s0, $s1
Bne $t0, $zero, exit
Addi $s0, $s0, -1
Exit: …

## Slide 22: Exercise
C code:
if (x > y)
x--;
Else
x = y--
What does the MIPS assembly look like?
  x in $s0, y in $s1
Notes: Slt $t0, $s0, $s1
Beq $t0, $zero, else
Beq $s0, $s1, else #if starts after this
Addi $s0, $s0, -1
J Exit
Else: add $s0, $s1, $zero
Addi $s1, $s1, -1
Exit:

## Slide 23: Exercise
C code:
for (i = 0; i < n; i++)
v[i] = 0;
What does the MIPS assembly look like?
  i in $s0, n in $s1, v in $s2
Notes: add $s0, $zero, $zero
Loop: slt $t0, $s0, $s1
beq $t0, $zero, Exit
sll $t1, $s0, 2 # let’s us index v
add $t1, $t1, $s2
sw $zero, 0($t1)
j Loop
Exit: