## Slide 1: Parallelism
Chapter 6
Notes: Why Parallelism?
Heat (power) & energy
Difference between power and energy?

## Slide 2: Strong vs Weak Scaling
Strong scaling: problem size fixed
  As in example
Weak scaling: problem size proportional to number of processors
  10 processors, 10 × 10 matrix
    Time = 20 × tadd
  100 processors, 32 × 32 matrix
    Time = 10 × tadd + 1000/100 × tadd = 20 × tadd
  Constant performance in this example
Notes: Exception: memory hierarchy!

## Slide 3: Instruction and Data Streams
An alternate classification
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Xeon e5345
SPMD: Single Program Multiple Data
  A parallel program on a MIMD computer
  Conditional code for different processors
§6.3 SISD, MIMD, SIMD, SPMD, and Vector

## Slide 4: Example: DAXPY (Y = a × X + Y)
Conventional MIPS code
l.d $f0,a($sp) ;load scalar a addiu r4,$s0,#512 ;upper bound of what to load loop: l.d $f2,0($s0) ;load x(i) mul.d $f2,$f2,$f0 ;a × x(i) l.d $f4,0($s1) ;load y(i) add.d $f4,$f4,$f2 ;a × x(i) + y(i) s.d $f4,0($s1) ;store into y(i) addiu $s0,$s0,#8 ;increment index to x addiu $s1,$s1,#8 ;increment index to y subu $t0,r4,$s0 ;compute bound bne $t0,$zero,loop ;check if done
Vector MIPS code
l.d $f0,a($sp) ;load scalar a lv $v1,0($s0) ;load vector x mulvs.d $v2,$v1,$f0 ;vector-scalar multiply lv $v3,0($s1) ;load vector y addv.d $v4,$v2,$v3 ;add y to product sv $v4,0($s1) ;store the result

## Slide 5: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to MIPS
  32 × 64-element registers (64-bit elements)
  Vector instructions
    lv, sv: load/store vector
    addv.d: add vectors of double
    addvs.d: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth

## Slide 6: Vector vs. Scalar
Vector architectures and compilers
  Simplify data-parallel programming
  Explicit statement of absence of loop-carried dependences
    Reduced checking in hardware
  Regular access patterns benefit from interleaved and burst memory
  Avoid control hazards by avoiding loops
More general than ad-hoc media extensions (such as MMX, SSE)
  Better match with compiler technology

## Slide 7: SIMD
Operate elementwise on vectors of data
  E.g., MMX and SSE instructions in x86
    Multiple data elements in 128-bit wide registers
All processors execute the same instruction at the same time
  Each with different data address, etc.
Simplifies synchronization
Reduced instruction control hardware
Works best for highly data-parallel applications

## Slide 8: Vector vs. Multimedia Extensions
Vector instructions have a variable vector width, multimedia extensions have a fixed width
Vector instructions support strided access, multimedia extensions do not
Vector units can be combination of pipelined and arrayed functional units:

## Slide 9: Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)
§6.4 Hardware Multithreading

## Slide 10: Simultaneous Multithreading
In multiple-issue dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Example: Intel Pentium-4 HT
  Two threads: duplicated registers, shared function units and caches
Notes: Think about a dual-issue chip, and how we talked about low utilization

## Slide 11: Multithreading Example

## Slide 12: Future of Multithreading
Will it survive? In what form?
Power considerations  simplified microarchitectures
  Simpler forms of multithreading
Tolerating cache-miss latency
  Thread switch may be most effective
Multiple simple cores might share resources more effectively

## Slide 13: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)
§6.5 Multicore and Other Shared Memory Multiprocessors
Notes: Sometimes people use SMP for Symmetric Multiprocessor, though this conflates with UMA.

## Slide 14: Example: Sum Reduction
Sum 100,000 numbers on 100 processor UMA

## Slide 15: Example: Sum Reduction
Sum 100,000 numbers on 100 processor UMA
  Each processor has ID: 0 ≤ Pn ≤ 99
  Partition 1000 numbers per processor
  Initial summation on each processor
  sum[Pn] = 0; for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1) sum[Pn] = sum[Pn] + A[i];
Now need to add these partial sums
  Reduction: divide and conquer
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps

## Slide 16: Example: Sum Reduction
half = 100;
repeat
synch();
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
/* Conditional sum needed when half is odd;
Processor0 gets missing element */
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);

## Slide 17: History of GPUs
Early video cards
  Frame buffer memory with address generation for video output
3D graphics processing
  Originally high-end computers (e.g., SGI)
  Moore’s Law  lower cost, higher density
  3D graphics cards for PCs and game consoles
Graphics Processing Units
  Processors oriented to 3D graphics tasks
  Vertex/pixel processing, shading, texture mapping, rasterization
§6.6 Introduction to Graphics Processing Units

## Slide 18: Graphics in the System

## Slide 19: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)

## Slide 20: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors

## Slide 21: Example: NVIDIA Tesla
Streaming Processors
  Single-precision FP and integer units
  Each SP is fine-grained multithreaded
Warp: group of 32 threads
  Executed in parallel, SIMD style
    8 SPs × 4 clock cycles
  Hardware contexts for 24 warps
    Registers, PCs, …

## Slide 22: Classifying GPUs
Don’t fit nicely into SIMD/MIMD model
  Conditional execution in a thread allows an illusion of MIMD
    But with performance degredation
    Need to write general purpose code with care
 | Static: Discovered at Compile Time | Dynamic: Discovered at Runtime
Instruction-Level Parallelism | VLIW | Superscalar
Data-Level Parallelism | SIMD or Vector | Tesla Multiprocessor

## Slide 23: GPU Memory Structures
Notes: CUDA thread -> one iteration of a loop (with SIMD instructions
Thread block -> one vectorized loop
Grid -> vectorized loop made up of several thread blocks

## Slide 24: Putting GPUs into Perspective
Feature | Multicore with SIMD | GPU
SIMD processors | 4 to 8 | 8 to 16
SIMD lanes/processor | 2 to 4 | 8 to 16
Multithreading hardware support for SIMD threads | 2 to 4 | 16 to 32
Typical ratio of single precision to double-precision performance | 2:1 | 2:1
Largest cache size | 8 MB | 0.75 MB
Size of memory address | 64-bit | 64-bit
Size of main memory | 8 GB to 256 GB | 4 GB to 6 GB
Memory protection at level of page | Yes | Yes
Demand paging | Yes | No
Integrated scalar processor/SIMD processor | Yes | No
Cache coherent | Yes | No
Notes: Extreme data locality => only small caches are necessary.

## Slide 25: Guide to GPU Terms