## Slide 1: Parallelism
Chapter 6
Notes: Why Parallelism?
Heat (power) & energy
Difference between power and energy?

## Slide 2: Multithreading Example

## Slide 3: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)
§6.5 Multicore and Other Shared Memory Multiprocessors
Notes: Sometimes people use SMP for Symmetric Multiprocessor, though this conflates with UMA.

## Slide 4: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors

## Slide 5: Classifying GPUs
Don’t fit nicely into SIMD/MIMD model
  Conditional execution in a thread allows an illusion of MIMD
    But with performance degredation
    Need to write general purpose code with care
 | Static: Discovered at Compile Time | Dynamic: Discovered at Runtime
Instruction-Level Parallelism | VLIW | Superscalar
Data-Level Parallelism | SIMD or Vector | Tesla Multiprocessor

## Slide 6: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors
§6.7 Clusters, WSC, and Other Message-Passing MPs

## Slide 7: Loosely Coupled Clusters
Network of independent computers
  Each has private memory and OS
  Connected using I/O system
    E.g., Ethernet/switch, Internet
Suitable for applications with independent tasks
  Web servers, databases, simulations, …
High availability, scalable, affordable
Problems
  Administration cost (prefer virtual machines)
  Low interconnect bandwidth
    c.f. processor/memory bandwidth on an SMP
Notes: A lot of supercomputers use message passing, but as one large system, vs. clusters…

## Slide 8: Sum Reduction (Again)
Sum 100,000 on 100 processors
First distribute 100 numbers to each
  The do partial sums
  sum = 0; for (i = 0; i<1000; i = i + 1) sum = sum + AN[i];
Reduction
  Half the processors send, other half receive and add
  The quarter send, quarter receive and add, …

## Slide 9: Sum Reduction (Again)
Given send() and receive() operations
  limit = 100; half = 100;/* 100 processors */ repeat half = (half+1)/2; /* send vs. receive dividing line */ if (Pn >= half && Pn < limit) send(Pn - half, sum); if (Pn < (limit/2)) sum = sum + receive(); limit = half; /* upper limit of senders */ until (half == 1); /* exit with final sum */
  Send/receive also provide synchronization
  Assumes send/receive take similar time to addition
Notes: There’s lots of details to how send() and receive() work
In real life you’d probably be using MPI

## Slide 10: Grid Computing
Separate computers interconnected by long-haul networks
  E.g., Internet connections
  Work units farmed out, results sent back
Can make use of idle time on PCs
  E.g., SETI@home, World Community Grid

## Slide 11: Interconnection Networks
Network topologies
  Arrangements of processors, switches, and links
§6.8 Introduction to Multiprocessor Network Topologies
Bus
Ring
2D Mesh
N-cube (N = 3)
Fully connected

## Slide 12: Multistage Networks

## Slide 13: Network Characteristics
Performance
  Latency per message (unloaded network)
  Throughput
    Link bandwidth
    Total network bandwidth
    Bisection bandwidth
  Congestion delays (depending on traffic)
Cost
Power
Routability in silicon
Notes: Fully connected total bandwidth: P(P-1)/2 (sum of (P-1)+(P-2)+(P-3)…+1+0)
Full connected bisection bandwith: (P/2)^2

## Slide 14: Parallel Benchmarks
Linpack: matrix linear algebra
SPECrate: parallel run of SPEC CPU programs
  Job-level parallelism
SPLASH: Stanford Parallel Applications for Shared Memory
  Mix of kernels and applications, strong scaling
NAS (NASA Advanced Supercomputing) suite
  computational fluid dynamics kernels
PARSEC (Princeton Application Repository for Shared Memory Computers) suite
  Multithreaded applications using Pthreads and OpenMP
§6.10 Multiprocessor Benchmarks and Performance Models

## Slide 15: Code or Applications?
Traditional benchmarks
  Fixed code and data sets
Parallel programming is evolving
  Should algorithms, programming languages, and tools be part of the system?
  Compare systems, provided they implement a given application
  E.g., Linpack, Berkeley Design Patterns
Would foster innovation in approaches to parallelism

## Slide 16: Modeling Performance
Assume performance metric of interest is achievable GFLOPs/sec
  Measured using computational kernels from Berkeley Design Patterns
Arithmetic intensity of a kernel
  FLOPs per byte of memory accessed
For a given computer, determine
  Peak GFLOPS (from data sheet)
  Peak memory bytes/sec (using Stream benchmark)

## Slide 17: Roofline Diagram
Attainable GPLOPs/sec
= Max ( Peak Memory BW × Arithmetic Intensity, Peak FP Performance )

## Slide 18: Comparing Systems
Example: Opteron X2 vs. Opteron X4
  2-core vs. 4-core, 2× FP performance/core, 2.2GHz vs. 2.3GHz
  Same memory system
To get higher performance on X4 than X2
  Need high arithmetic intensity
  Or working set must fit in X4’s 2MB L-3 cache

## Slide 19: Optimizing Performance
Optimize FP performance
  Balance adds & multiplies
  Improve superscalar ILP and use of SIMD instructions
Optimize memory usage
  Software prefetch
    Avoid load stalls
  Memory affinity
    Avoid non-local data accesses

## Slide 20: Optimizing Performance
Choice of optimization depends on arithmetic intensity of code
Arithmetic intensity is not always fixed
  May scale with problem size
  Caching reduces memory accesses
    Increases arithmetic intensity

## Slide 21: i7-960 vs. NVIDIA Tesla 280/480
§6.11 Real Stuff: Benchmarking and Rooflines i7 vs. Tesla

## Slide 22: Rooflines

## Slide 23: Benchmarks

## Slide 24: Performance Summary
GPU (480) has 4.4 X the memory bandwidth
  Benefits memory bound kernels
GPU has 13.1 X the single precision throughout, 2.5 X the double precision throughput
  Benefits FP compute bound kernels
CPU cache prevents some kernels from becoming memory bound when they otherwise would on GPU
GPUs offer scatter-gather, which assists with kernels with strided data
Lack of synchronization and memory consistency support on GPU limits performance for some kernels

## Slide 25: Multi-threading DGEMM
§6.12 Going Faster: Multiple Processors and Matrix Multiply
Use OpenMP:
void dgemm (int n, double* A, double* B, double* C)
{
#pragma omp parallel for
for ( int sj = 0; sj < n; sj += BLOCKSIZE )
for ( int si = 0; si < n; si += BLOCKSIZE )
for ( int sk = 0; sk < n; sk += BLOCKSIZE )
do_block(n, si, sj, sk, A, B, C);
}

## Slide 26: Multithreaded DGEMM

## Slide 27: Multithreaded DGEMM

## Slide 28: Fallacies
Amdahl’s Law doesn’t apply to parallel computers
  Since we can achieve linear speedup
  But only on applications with weak scaling
Peak performance tracks observed performance
  Marketers like this approach!
  But compare Xeon with others in example
  Need to be aware of bottlenecks
§6.13 Fallacies and Pitfalls

## Slide 29: Pitfalls
Not developing the software to take account of a multiprocessor architecture
  Example: using a single lock for a shared composite resource
    Serializes accesses, even if they could be done in parallel
    Use finer-granularity locking

## Slide 30: Concluding Remarks
Goal: higher performance by using multiple processors
Difficulties
  Developing parallel software
  Devising appropriate architectures
SaaS importance is growing and clusters are a good match
Performance per dollar and performance per Joule drive both mobile and WSC
§6.14 Concluding Remarks

## Slide 31: Concluding Remarks (con’t)
SIMD and vector operations match multimedia applications and are easy to program