## Slide 1: ECC, Instructions
Instructor: Robert Utterback
Lecture 12

## Slide 2: Set-Reset Latch (S-R Latch)
A pair of cross-coupled NOR gates
  Unclocked
    Do not have a clock input
  Can store an internal value
    Q represent the current state
Notes: Draw a truth table for this (inputs are Q_old, ~Q_old, R and S, outputs are Q_new and ~Q_new)

## Slide 3: Flip-flops
D-Latch
  Clock input C
  Data input D

## Slide 4: D Flip Flop
D Flip Flop with a Falling-Edge Trigger

## Slide 5: Register Files
A register file consists of a set of registers that can be read and written by supplying a register number
  Built from an array of D Flip-Flops
  A decoder is used to select a register in the register file

## Slide 6: Register Files
Register Files
  Can be used to build small memory
  Too costly to build large amount of memory
Large Scale Memory
  Static random access memories (SRAM)
  Dynamic random access memories (DRAM)

## Slide 7: SRAM and DRAM
SRAM
  Fast but costly
  Small amount
  Used for Computer Cache
DRAM
  Slow but less costly
  Large amount
  Used for Computer Main Memory

## Slide 8: Error Detection and Correction
Error in large memory
  Potential of data corruption
Error Checking Code
  Detect possible corruption data
Error Correction Code
  Correct possible corruption data

## Slide 9: Parity Code
Mechanism of (Even) Parity Code
  Count the number of 1s in a word
  If the number of 1s is odd
    1
  If the number of 1s is even
    0
  Example
  Data Parity bit
  01100111 1
  When a word is written into memory, the parity bit is also calculated and written
  When a word is read, if the parity bit does not match, there is an error

## Slide 10: Parity Scheme
1-bit Parity Scheme
  Can detect at most 1 bit of error
  Cannot detect 2 bits of error
  Cannot correct an error

## Slide 11: Error Correction Code (ECC)
Error Correction Code (ECC)
  Can correct certain errors
  Requires more bits
    7 bits for 64-bit word
    8 bits for 128-bit word
  Most computers use ECC for
    Detection of 2 bits of error
    Correction of 1 bit of error

## Slide 12: Instructions: Language of the Computer (Ch 2)
Instructor: Robert Utterback
Lecture 12

## Slide 13: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction
Notes: Instructions: commands that a computer can understand

## Slide 14: CISC and RISC
CISC (complex instruction set computer)
  VAX, Intel X86, IBM 360/370, etc.
RISC (reduced instruction set computer)
  MIPS, DEC Alpha, SUN Sparc, IBM RS6000
Boundaries have blurred
Modern CPUs utilize features of both
Notes: Basically two camps…
RISC are simple instructions, that are easier to implement and also to understand
CISC is complex instructions, harder to understand and implement, but each instruction can do more complicated and fancy things.

## Slide 15: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E

## Slide 16: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
How about a = b + c + d?
§2.2 Operations of the Computer Hardware
Notes: add a, b, c
add a, a, d
OR
Add t0, b, c
add a, t0, d

## Slide 17: ISA Design
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware
Notes: A, b, and c are just abstract locations here…

## Slide 18: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 19: More Arithmetic Example
C code:
f = g + h + i + j + k;
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, t0, i # temp t1 = t0 + i add t2, t1, j # temp t2 = t1 + j add f, t2, k # f = t2 + k
Do we really need three registers?

## Slide 20: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Why only 32?
§2.3 Operands of the Computer Hardware
Notes: For now, just s and t. We’ll get to why these names, and use the rest of the registers, in 2.8.

## Slide 21: ISA Design
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations

## Slide 22: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 23: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4

## Slide 24: Byte Ordering
Little-endian byte order
  With the low-order byte at the starting address
  Example: Intel, DEC
Big-endian byte order
  With the high-order byte at the starting address
  Example: HP, IBM, Motorola 68000
  Internet standard byte ordering
Format 25610 in little-endian and big-endian using 16 bits
Format
Value
Little-Endian
00000000 00000001
Big-Endian
00000001 00000000
Notes: MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 25: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register
Notes: Need to pause a define an array, e.g. just a fixed area in memory that we can treat as a “vector” of memory words…no operations defined on it, can’t add to its size….

## Slide 26: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
Notes: Exercise: what about A[2] = A[0] + A[1], with base of A in $s0?