## Slide 1: Parallelism
Chapter 6
Notes: Why Parallelism?
Heat (power) & energy
Difference between power and energy?

## Slide 2: Introduction
Goal: connecting multiple computers to get higher performance
  Multiprocessors
  Scalability, availability, power efficiency
Task-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing program
  Single program run on multiple processors
Multicore microprocessors
  Chips with multiple processors (cores)
§6.1 Introduction

## Slide 3: Hardware and Software
Hardware
  Serial: e.g., Pentium 4
  Parallel: e.g., quad-core Xeon e5345
Software
  Sequential: e.g., matrix multiplication
  Concurrent: e.g., operating system
Sequential/concurrent software can run on serial/parallel hardware
  Challenge: making effective use of parallel hardware

## Slide 4: Parallelism in the Book
§2.11: Parallelism and Instructions
  Synchronization
§3.6: Parallelism and Computer Arithmetic
  Subword Parallelism
§4.10: Parallelism and Advanced Instruction-Level Parallelism
§5.10: Parallelism and Memory Hierarchies
  Cache Coherence

## Slide 5: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead
§6.2 The Difficulty of Creating Parallel Processing Programs
Notes: Reporting analogy – equal sized pieces, communication overhead, balancing the load, time to synchronize
The more processors (reporters), the harder this coordination becomes…

## Slide 6: Amdahl’s Law
Notes: Who remembers Amdahl’s law? If not the details, then what is means at a high level…

## Slide 7: Amdahl’s Law
Sequential part can limit speedup
Example: 100 processors, 90× speedup?
  Tnew = Tparallelizable/100 + Tsequential
  Solving: Fparallelizable = 0.999
Need sequential part to be 0.1% of original time
Notes: Speedup = T_old / T_new = T_old / (T_par/100 + T_seq)
= 1/( (T_par/100/T_old) + (T_seq/T_old) = 1 / ((F_par/100) + F_seq)

## Slide 8: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)
Assumes load can be balanced across processors
Notes: Now I want you do repeat these calculations with a 100x100 matrix.

## Slide 9: Scaling Example (cont)
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9 (99% of potential)
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91 (91% of potential)
Assuming load balanced

## Slide 10: Strong vs Weak Scaling
Strong scaling: problem size fixed
  As in example
Weak scaling: problem size proportional to number of processors
  10 processors, 10 × 10 matrix
    Time = 20 × tadd
  100 processors, 32 × 32 matrix
    Time = 10 × tadd + 1000/100 × tadd = 20 × tadd
  Constant performance in this example
Notes: Exception: memory hierarchy!

## Slide 11: Instruction and Data Streams
An alternate classification
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Xeon e5345
SPMD: Single Program Multiple Data
  A parallel program on a MIMD computer
  Conditional code for different processors
§6.3 SISD, MIMD, SIMD, SPMD, and Vector

## Slide 12: Example: DAXPY (Y = a × X + Y)
Conventional MIPS code
l.d $f0,a($sp) ;load scalar a addiu r4,$s0,#512 ;upper bound of what to load loop: l.d $f2,0($s0) ;load x(i) mul.d $f2,$f2,$f0 ;a × x(i) l.d $f4,0($s1) ;load y(i) add.d $f4,$f4,$f2 ;a × x(i) + y(i) s.d $f4,0($s1) ;store into y(i) addiu $s0,$s0,#8 ;increment index to x addiu $s1,$s1,#8 ;increment index to y subu $t0,r4,$s0 ;compute bound bne $t0,$zero,loop ;check if done
Vector MIPS code
l.d $f0,a($sp) ;load scalar a lv $v1,0($s0) ;load vector x mulvs.d $v2,$v1,$f0 ;vector-scalar multiply lv $v3,0($s1) ;load vector y addv.d $v4,$v2,$v3 ;add y to product sv $v4,0($s1) ;store the result

## Slide 13: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to MIPS
  32 × 64-element registers (64-bit elements)
  Vector instructions
    lv, sv: load/store vector
    addv.d: add vectors of double
    addvs.d: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth

## Slide 14: Vector vs. Scalar
Vector architectures and compilers
  Simplify data-parallel programming
  Explicit statement of absence of loop-carried dependences
    Reduced checking in hardware
  Regular access patterns benefit from interleaved and burst memory
  Avoid control hazards by avoiding loops
More general than ad-hoc media extensions (such as MMX, SSE)
  Better match with compiler technology

## Slide 15: SIMD
Operate elementwise on vectors of data
  E.g., MMX and SSE instructions in x86
    Multiple data elements in 128-bit wide registers
All processors execute the same instruction at the same time
  Each with different data address, etc.
Simplifies synchronization
Reduced instruction control hardware
Works best for highly data-parallel applications

## Slide 16: Vector vs. Multimedia Extensions
Vector instructions have a variable vector width, multimedia extensions have a fixed width
Vector instructions support strided access, multimedia extensions do not
Vector units can be combination of pipelined and arrayed functional units: