## Slide 1: 3.4: Division
Instructor: Robert Utterback
Lecture 30

## Slide 2: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low
Notes: Multiplier is in the right half of the product register.

## Slide 3: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd
Notes: This last is a pseudoinstruction

## Slide 4: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 5: Division Hardware
Initially dividend
Initially divisor in left half
First version of Division Hardware
  32-bit quotient
  64-bit ALU
  64-bit remainder
Notes: Divisor starts in left half of divisor register, remainder initialized to dividend

## Slide 6: First Version Division Hardware
Initially dividend
Initially divisor in left half
Notes: Example: Fill out a table for 7/2
Table:
Iteration, Step (1,2b,3), Quotient, Divisor, Remainder

## Slide 7: Example
7/2

## Slide 8: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both
Notes: Remainder in left half, Dividend in right half

## Slide 9: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT division) generate multiple quotient bits per step
  Still require multiple steps

## Slide 10: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 11: Example Revisit
A better way to do 7/2?
  7>>2
  SRL
Most compiler will replace divide by power of 2 using right shift operations

## Slide 12: Summary
Multiplication
  First version of multiplication
  Optimized multiplication
Division

## Slide 13: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point
Notes: Normalized: >= 1 < 10

## Slide 14: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 15: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Not really, though
  Exponent is slightly more complicated
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Notes: Try an example on
Sign: 1
Exponent: 0 0 0 0 0 0 0 1
Fraction: 0 1 0 (0…)
Which is -1.25 * 2^1 = -2.5, exception not really

## Slide 16: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Notes: See p.200 for the reason behind biasing --- basically, it makes comparison a lot easier, hence sorting can be done efficiently.
The bias makes the most negative exponent (which makes a small number) 0…0 and the most positive exponent 1..1
Now let’s do the example of p.202
Now example on p.201