## Slide 1: Instructions: Language of the Computer (Ch 2)
Instructor: Robert Utterback
Lecture 12

## Slide 2: Review
What ISA are we using?
Is MIPS RISC (A) or CISC (B)?
(Our) MIPS has __ registers
How many bits needed to address 32 registers?
§2.1 Introduction
A | VAX
B | Intel x86
C | Sparc
D | MIPS
A | 8
B | 16
C | 32
D | 64
Notes: D, A, C, 5

## Slide 3: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
§2.3 Operands of the Computer Hardware
Notes: It’d be annoying to just use numbers for registers, so we have a few mnemonics that the assembler helps us with.
For now, just s and t. We’ll get to why these names, and use the rest of the registers, in 2.8.

## Slide 4: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 5: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
Notes: Very important to understand memory and visualize it in your head!

## Slide 6: Byte Ordering
Little-endian byte order
  With the low-order byte at the starting address
  Example: Intel, DEC
Big-endian byte order
  With the high-order byte at the starting address
  Example: HP, IBM, Motorola 68000
  Internet standard byte ordering
Format 25610 in little-endian and big-endian using 16 bits
Format
Value
Little-Endian
00000000 00000001
Big-Endian
00000001 00000000
Notes: MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 7: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register
Notes: For now, we are assuming each ”slot” in the array is a word. We will generalize this to other sizes later!
Need to pause a define an array, e.g. just a fixed area in memory that we can treat as a “vector” of memory words…no operations defined on it, can’t add to its size….

## Slide 8: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 9: Exercise
C code:
A[2] = A[0] - A[1];
  Base address of A in $s0
Notes: lw $t0, 0($s0)
lw $t1, 4($s0)
sub $t0, $t0, $t1
sw $t0, 8($s0)

## Slide 10: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!
Notes: Simple example: 2 registers, 3 data words. Want to do x + y + z, must spill registers.

## Slide 11: Adding Constants
C code:
a = b + 1;
Data must be in registers
Load from memory just for a constant?

## Slide 12: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction
Notes: Although in some sense, this IS still loading from memory, since the instructions are stored in memory. Surprise!

## Slide 13: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 14: Representing Numbers (review)
Section 2.4

## Slide 15: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers
Notes: Quick review of section 2.4: we’ve already seen this stuff. Read 2.4 if you need a review or didn’t quite catch it the first time.

## Slide 16: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 17: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 18: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 19: Sign Extension
Representing a number using more bits
  Ex: load 8-bit value into 16-bit registers
  Preserve the numeric value
Examples: 8-bit to 16-bit
  +2: 0000 0010 =>
  –2: 1111 1110 =>
Notes: STOP! This is something not covered in app B!
That is -2 in 8 bits…Q: What would it be in 16 bits?

## Slide 20: Sign Extension
Representing a number using more bits
  Ex: load 8-bit value into 16-bit registers
  Preserve the numeric value
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 21: Sign Extension
Representing a number using more bits
  Ex: load 8-bit value into 16-bit registers
  Preserve the numeric value
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
In MIPS instruction set
  lb, lh: extend loaded byte/halfword
Replicate the sign bit to the left
Notes: As oppose to lbu and lhu, which will fill with 0s always.
Something we want to do that if we are representing unsigned numbers. For example, we might be representing “chars” (characters) with an unsigned byte. This lets us map 0-127 to characters.
Note about alignment restriction: *you* must ensure 4-bit alignment when using sw/lw. You don’t when using lb, lh, etc. But this alignment is still happening in the background – the hardware figures out which *word* that byte is in, loads in, then picks out the byte/halfword you want

## Slide 22: Representing Instructions
Section 2.5

## Slide 23: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23
§2.5 Representing Instructions in the Computer

## Slide 24: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: There are a few different formats; here’s one. The “op” and “funct” *together* tell us exactly what instruction is happening.
You don’t have to memorize stuff like this – it’s on your ”green sheet” and I always let you use it on exams.

## Slide 25: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: By the way, why 5 bits for the registers?
Sub is op=0, funct=34., NOR=27, OR=25 (funct)
Most R format instructions have op=0 (I only know of 1 that does not)
So these are long strings of bits…difficult to read. But we have a bit of a shortcut.

## Slide 26: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000
Notes: It’s way too messy to always deal with bit strings…

## Slide 27: Example
What instruction is:
012a 8020 ?
add $s0, $t1, $t2
Notes: 0000 0001 0010 1010 1000 0000 0010 0000
000000 01001 01010 10000 00000 100000
Op = 0
Rs = 9
Rt = 10
Rd = 16
Shamt = 0
Funct = 32
So this is an add instruction.