## Slide 1: DataPath (4.3)
Lecture 35

## Slide 2: Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j
§4.1 Introduction

## Slide 3: Instruction Execution
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 4: CPU Overview

## Slide 5: Multiplexers
Can’t just join wires together
  Use multiplexers
Notes: What logic component can we use to choose between multiple inputs?

## Slide 6: Control
Notes: Typically we won’t show all these control wires b/c they make the picture messy. Instead we’ll just show a blue line segment going in to the appropriate place.

## Slide 7: Logic Design Basics
§4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 8: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 9: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 10: Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 11: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 12: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 13: Instruction Fetch
32-bit register
Increment by 4 for next instruction
Notes: Why do we need to increment by 4? So how big is the PC?

## Slide 14: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result
Notes: Why 5 bits?

## Slide 15: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 16: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch
Notes: What addressing mode do branch instructions use?

## Slide 17: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 18: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 19: R-Type/Load/Store Datapath

## Slide 20: Full Datapath

## Slide 21: ALU Control
ALU used for
  Load/Store: add
  Branch: subtract
  R-type: depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR
Notes: Why that relationship between add and subtract? Remember the picture of our ALU?
Need to generate these 4 ALU control bits based on the instruction we are currently executing..