## Slide 1: Arrays vs. Pointers
Instructor: Robert Utterback
Lecture 20
Notes: Arrays vs. pointers is the most important thing, though we’ll touch on some other tidbits to finish up chapter 2.

## Slide 2: Lazy Linkage
Indirection table
Stub: Loads routine ID, Jump to linker/loader
Linker/loader code
Dynamically mapped code
Notes: All problems in computer science can be solved by indirection.

## Slide 3: Effect of Compiler Optimization
Compiled with gcc for Pentium 4 under Linux
Notes: Notice that instruction count is lowest with O1, but best CPI is none! Best performance metric is just execution time!

## Slide 4: Effect of Language and Algorithm
Notes: Optimization doesn’t help quicksort as much b/c it’s a faster algorithm overall…

## Slide 5: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 6: Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers

## Slide 7: Example: Clearing and Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2
Notes: Using an index: adding to this, then calculating the memory address
Pointer: just keep the address you need directly, and add to this pointer value

## Slide 8: Comparison of Array vs. Ptr
Multiply “strength reduced” to shift
Array version requires shift to be inside loop
  Part of index calculation for incremented i
  c.f. incrementing pointer
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer

## Slide 9: ARM & MIPS Similarities
ARM: the most popular embedded core
Similar basic set of instructions to MIPS
§2.16 Real Stuff: ARM Instructions
 | ARM | MIPS
Date announced | 1985 | 1985
Instruction size | 32 bits | 32 bits
Address space | 32-bit flat | 32-bit flat
Data alignment | Aligned | Aligned
Data addressing modes | 9 | 3
Registers | 15 × 32-bit | 31 × 32-bit
Input/output | Memory mapped | Memory mapped

## Slide 10: Compare and Branch in ARM
Uses condition codes for result of an arithmetic/logical instruction
  Negative, zero, carry, overflow
  Compare instructions to set condition codes without keeping the result
Each instruction can be conditional
  Top 4 bits of instruction word: condition value
  Can avoid branches over single instructions
Notes: Top 4 bits correspond to the 4 condition codes

## Slide 11: Instruction Encoding

## Slide 12: The Intel x86 ISA
Evolution with backward compatibility
  8080 (1974): 8-bit microprocessor
    Accumulator, plus 3 index-register pairs
  8086 (1978): 16-bit extension to 8080
    Complex instruction set (CISC)
  8087 (1980): floating-point coprocessor
    Adds FP instructions and register stack
  80286 (1982): 24-bit addresses, MMU
    Segmented memory mapping and protection
  80386 (1985): 32-bit extension (now IA-32)
    Additional addressing modes and operations
    Paged memory mapping as well as segments
§2.17 Real Stuff: x86 Instructions

## Slide 13: The Intel x86 ISA
Further evolution…
  i486 (1989): pipelined, on-chip caches and FPU
    Compatible competitors: AMD, Cyrix, …
  Pentium (1993): superscalar, 64-bit datapath
    Later versions added MMX (Multi-Media eXtension) instructions
    The infamous FDIV bug
  Pentium Pro (1995), Pentium II (1997)
    New microarchitecture (see Colwell, The Pentium Chronicles)
  Pentium III (1999)
    Added SSE (Streaming SIMD Extensions) and associated registers
  Pentium 4 (2001)
    New microarchitecture
    Added SSE2 instructions

## Slide 14: The Intel x86 ISA
And further…
  AMD64 (2003): extended architecture to 64 bits
  EM64T – Extended Memory 64 Technology (2004)
    AMD64 adopted by Intel (with refinements)
    Added SSE3 instructions
  Intel Core (2006)
    Added SSE4 instructions, virtual machine support
  AMD64 (announced 2007): SSE5 instructions
    Intel declined to follow, instead…
  Advanced Vector Extension (announced 2008)
    Longer SSE registers, more instructions
If Intel didn’t extend with compatibility, its competitors would!
  Technical elegance ≠ market success

## Slide 15: Basic x86 Registers

## Slide 16: Basic x86 Addressing Modes
Two operands per instruction
Source/dest operand | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate
Memory addressing modes
  Address in register
  Address = Rbase + displacement
  Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
  Address = Rbase + 2scale × Rindex + displacement

## Slide 17: x86 Instruction Encoding
Variable length encoding
  Postfix bytes specify addressing mode
  Prefix bytes modify operation
    Operand length, repetition, locking, …

## Slide 18: Implementing IA-32
Complex instruction set makes implementation difficult
  Hardware translates instructions to simpler microoperations
    Simple instructions: 1–1
    Complex instructions: 1–many
  Microengine similar to RISC
  Market share makes this economically viable
Comparable performance to RISC
  Compilers avoid complex instructions
Notes: Large Market share = high revenue = pay lots of people a lot of money to work on it

## Slide 19: ARM v8 Instructions
In moving to 64-bit, ARM did a complete overhaul
ARM v8 resembles MIPS
  Changes from v7:
    No conditional execution field
    Immediate field is 12-bit constant
    Dropped load/store multiple
    PC is no longer a GPR
    GPR set expanded to 32
    Addressing modes work for all word sizes
    Divide instruction
    Branch if equal/branch if not equal instructions
§2.18 Real Stuff: ARM v8 (64-bit) Instructions

## Slide 20: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity
§2.19 Fallacies and Pitfalls
Notes: But we still want to understand the assembly to understand the ISA and write better C code.

## Slide 21: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 22: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped
Notes: Give a quick example.

## Slide 23: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Make the common case fast
  4. Good design demands good compromises
Layers of software/hardware
  Compiler, assembler, hardware
MIPS: typical of RISC ISAs
  c.f. x86
§2.20 Concluding Remarks

## Slide 24: Concluding Remarks
Measure MIPS instruction executions in benchmark programs
  Consider making the common case fast
  Consider compromises
Instruction class | MIPS examples | SPEC2006 Int | SPEC2006 FP
Arithmetic | add, sub, addi | 16% | 48%
Data transfer | lw, sw, lb, lbu, lh, lhu, sb, lui | 35% | 36%
Logical | and, or, nor, andi, ori, sll, srl | 12% | 4%
Cond. Branch | beq, bne, slt, slti, sltiu | 34% | 8%
Jump | j, jr, jal | 2% | 0%