## Slide 1: The Memory Hierarchy
Chapter 5

## Slide 2: The Problem
Pick 1
  Fast memory
  Cheap (=> large) memory
Registers are fast, but we only have a few
SRAM larger, but slower
DRAM is dense but very slow
Disks are extremely dense but even slower

## Slide 3: The Fix: Hierarchy of Memory
Registers
Cache (SRAM)
Main Memory (DRAM)
Disks (HDD and/or SDD)
Notes: Relies on speculation to work correctly. We can’t always speculate correctly, but luckily we often can because of locality…

## Slide 4: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data
§5.1 Introduction

## Slide 5: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU
Notes: SRAM used to be on separate chips on the motherboard, but now they are built onto the same chip as the CPU

## Slide 6: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level
Notes: We will always be talking about inclusive memory hierarchy…

## Slide 7: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $500 – $1000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $10 – $20 per GB
Flash (USB stick, SSD)
  5000-50000ns, $0.75-$1.00 per GB
Magnetic disk
  5ms – 20ms, $0.05 – $0.10 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
§5.2 Memory Technologies
Notes: These are 2012 prices

## Slide 8: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge
  Must periodically be refreshed
    Read contents and write back
    Performed on a DRAM “row”

## Slide 9: Advanced DRAM Organization
Bits in a DRAM are organized as a rectangular array
  DRAM accesses an entire row
  Burst mode: supply successive words from a row with reduced latency
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
Quad data rate (QDR) DRAM
  Separate DDR inputs and outputs

## Slide 10: DRAM Generations
Year | Capacity | $/GB
1980 | 64Kbit | $1500000
1983 | 256Kbit | $500000
1985 | 1Mbit | $200000
1989 | 4Mbit | $50000
1992 | 16Mbit | $15000
1996 | 64Mbit | $10000
1998 | 128Mbit | $4000
2000 | 256Mbit | $1000
2004 | 512Mbit | $250
2007 | 1Gbit | $50

## Slide 11: DRAM Performance Factors
Row buffer
  Allows several words to be read and refreshed in parallel
Synchronous DRAM (SDRAM)
  Allows for consecutive accesses in bursts without needing to send each address
  Improves bandwidth
DRAM banking
  Allows simultaneous access to multiple DRAMs
  Improves bandwidth

## Slide 12: Increasing Memory Bandwidth
4-word wide memory
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  Bandwidth = 16 bytes / 17 cycles = 0.94 B/cycle
4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 B/cycle
Notes: 1 cycle to notice the miss, 15 cycles to transfer the words, 1 more to get from cache

## Slide 13: Flash Storage
Nonvolatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)
§6.4 Flash Storage
Notes: Big area of change/research currently! Lots of new technologies!
Some may already have an SSD on their laptops…

## Slide 14: Flash Types
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser (bits/area), but block-at-a-time access
  Cheaper per GB
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Not suitable for direct RAM or disk replacement
  Wear leveling: remap data to less used blocks
Notes: Flash is typically EEPROM, which we briefly talked about in Appendix B.
I don’t actually know that much about the specifics of the types of memory; it quickly gets into electrical engineering territory.

## Slide 15: Disk Storage
Nonvolatile, rotating magnetic storage
§6.3 Disk Storage

## Slide 16: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes proposed)
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads
  Rotational latency
  Data transfer
  Controller overhead

## Slide 17: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time
  4ms seek time + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms
Notes: This *seems* fast, but is super slow compared to other memory…

## Slide 18: Disk Performance Issues
Manufacturers quote average seek time
  Based on all possible seeks
  Locality and OS scheduling lead to smaller actual average seek times
Smart disk controller allocate physical sectors on disk
  Present logical sector interface to host
  SCSI, ATA, SATA
Disk drives include caches
  Prefetch sectors in anticipation of access
  Avoid seek and rotational delay
Notes: There are lots of other memory technologies. Magnetic tape, for example, is EXTREMELY slow but very dense.
Lots of companies used to use tape for backups, and a few still do. I bet there’s warehouses worth of old tape backups sittings somewhere.

## Slide 19: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
How do we know if the data is present?
Where do we look?
Notes: The cache is smaller than the rest of memory, so we can only store some things in here.
Brainstorm some ideas on how to do this?

## Slide 20: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits
Notes: BTW, what’s the problem with this approach?
We may have two slots and also use two memory locations. Theoretically they should both fit in cache, but if they both map to the same slot they don’t!

## Slide 21: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 22: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
Notes: Accesses:
22, 10 110
26, 11 010
22, 10 110
26, 11 010
16, 10 000
3, 00 011
16, 10 000
18, 10 010
16, 10 000