## Slide 1: Parallelism
Chapter 6
Notes: Why Parallelism?
Heat (power) & energy
Difference between power and energy?

## Slide 2: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead
§6.2 The Difficulty of Creating Parallel Processing Programs
Notes: Reporting analogy – equal sized pieces, communication overhead, balancing the load, time to synchronize
The more processors (reporters), the harder this coordination becomes…

## Slide 3: Amdahl’s Law
Sequential part can limit speedup
Example: 100 processors, 90× speedup?
  Tnew = Tparallelizable/100 + Tsequential
  Solving: Fparallelizable = 0.999
Need sequential part to be 0.1% of original time
Notes: Speedup = T_old / T_new = T_old / (T_par/100 + T_seq)
= 1/( (T_par/100/T_old) + (T_seq/T_old) = 1 / ((F_par/100) + F_seq)
Note that parts of a problem may be parallelizable but not perfectly…

## Slide 4: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)
Assumes load can be balanced across processors
Notes: Now I want you do repeat these calculations with a 100x100 matrix.

## Slide 5: Scaling Example (cont)
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9 (99% of potential)
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91 (91% of potential)
Assuming load balanced

## Slide 6: Strong vs Weak Scaling
Strong scaling: problem size fixed
  As in example
Weak scaling: problem size proportional to number of processors
  10 processors, 10 × 10 matrix
    Time = 20 × tadd
  100 processors, 32 × 32 matrix
    Time = 10 × tadd + 1000/100 × tadd = 20 × tadd
  Constant performance in this example
Notes: Exception: memory hierarchy!

## Slide 7: Instruction and Data Streams
An alternate classification
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Xeon e5345
SPMD: Single Program Multiple Data
  A parallel program on a MIMD computer
  Conditional code for different processors
§6.3 SISD, MIMD, SIMD, SPMD, and Vector

## Slide 8: Example: DAXPY (Y = a × X + Y)
Conventional MIPS code
l.d $f0,a($sp) ;load scalar a addiu r4,$s0,#512 ;upper bound of what to load loop: l.d $f2,0($s0) ;load x(i) mul.d $f2,$f2,$f0 ;a × x(i) l.d $f4,0($s1) ;load y(i) add.d $f4,$f4,$f2 ;a × x(i) + y(i) s.d $f4,0($s1) ;store into y(i) addiu $s0,$s0,#8 ;increment index to x addiu $s1,$s1,#8 ;increment index to y subu $t0,r4,$s0 ;compute bound bne $t0,$zero,loop ;check if done
Vector MIPS code
l.d $f0,a($sp) ;load scalar a lv $v1,0($s0) ;load vector x mulvs.d $v2,$v1,$f0 ;vector-scalar multiply lv $v3,0($s1) ;load vector y addv.d $v4,$v2,$v3 ;add y to product sv $v4,0($s1) ;store the result
Notes: Note dependencies in conventional mode.
Code size is a bit misleading: if you needed to DAXPY more elements than fit in a vector, still need the loop operations…

## Slide 9: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to MIPS
  32 × 64-element registers (64-bit elements)
  Vector instructions
    lv, sv: load/store vector
    addv.d: add vectors of double
    addvs.d: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth
Notes: Instead of fixed width SIMD

## Slide 10: Vector vs. Scalar
Vector architectures and compilers
  Simplify data-parallel programming
  Explicit statement of absence of loop-carried dependences
    Reduced checking in hardware
  Regular access patterns benefit from interleaved and burst memory
  Avoid control hazards by avoiding loops
More general than ad-hoc media extensions (such as MMX, SSE)
  Better match with compiler technology

## Slide 11: SIMD
Operate elementwise on vectors of data
  E.g., MMX and SSE instructions in x86
    Multiple data elements in 128-bit wide registers
All processors execute the same instruction at the same time
  Each with different data address, etc.
Simplifies synchronization
Reduced instruction control hardware
Works best for highly data-parallel applications
Notes: SIMD in general just means single instruction, multiple data, but most people use it when talking about media extensions: SSE, AVX, etc.

## Slide 12: Vector vs. Multimedia Extensions
Vector instructions have a variable vector width, multimedia extensions have a fixed width
Vector instructions support strided access, multimedia extensions do not
Vector units can be combination of pipelined and arrayed functional units:
Notes: Didn’t show, but you can specify how much of a vector register you want to use for an operation.
More specifically, # of operations for vector is not in the opcode (like AVX,SSE) but in a register.
Though I’m pretty sure later Intel media extensions do support strided access and gather/scatter… (maybe manual only?)

## Slide 13: Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)
§6.4 Hardware Multithreading

## Slide 14: Simultaneous Multithreading
In multiple-issue dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Example: Intel Pentium-4 HT
  Two threads: duplicated registers, shared function units and caches
Notes: Think about a dual-issue chip, and how we talked about low utilization

## Slide 15: Multithreading Example
Notes: Coarse MT must take time to load up pipeline. Fine MT requires very fast thread-switching time and still not full utilization.

## Slide 16: Future of Multithreading
Will it survive? In what form?
Power considerations  simplified microarchitectures
  Simpler forms of multithreading
Tolerating cache-miss latency
  Thread switch may be most effective
Multiple simple cores might share resources more effectively

## Slide 17: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)
§6.5 Multicore and Other Shared Memory Multiprocessors
Notes: Sometimes people use SMP for Symmetric Multiprocessor, though this conflates with UMA.

## Slide 18: Example: Sum Reduction
Sum 100,000 numbers on 100 processor UMA

## Slide 19: Example: Sum Reduction
Sum 100,000 numbers on 100 processor UMA
  Each processor has ID: 0 ≤ Pn ≤ 99
  Partition 1000 numbers per processor
  Initial summation on each processor
  sum[Pn] = 0; for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1) sum[Pn] = sum[Pn] + A[i];
Now need to add these partial sums
  Reduction: divide and conquer
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps

## Slide 20: Example: Sum Reduction
half = 100;
repeat
synch();
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
/* Conditional sum needed when half is odd;
Processor0 gets missing element */
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);

## Slide 21: History of GPUs
Early video cards
  Frame buffer memory with address generation for video output
3D graphics processing
  Originally high-end computers (e.g., SGI)
  Moore’s Law  lower cost, higher density
  3D graphics cards for PCs and game consoles
Graphics Processing Units
  Processors oriented to 3D graphics tasks
  Vertex/pixel processing, shading, texture mapping, rasterization
§6.6 Introduction to Graphics Processing Units

## Slide 22: Graphics in the System

## Slide 23: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)
Notes: Now OpenCL, like CUDA but for many GPU makers

## Slide 24: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors
Notes: Each GPU is split up into many (8-16) multithreaded SIMD processors (streaming multiprocessor).
Each of these is split up into many SIMD lanes (streaming processors), and use multithreading to support up to 32 separate instruction streams.

## Slide 25: Example: NVIDIA Tesla
Streaming Processors
  Single-precision FP and integer units
  Each SMP is fine-grained multithreaded
Warp: group of 32 threads
  Executed in parallel, SIMD style
    8 SPs × 4 clock cycles
  Hardware contexts for 24 warps
    Registers, PCs, …

## Slide 26: Classifying GPUs
Don’t fit nicely into SIMD/MIMD model
  Conditional execution in a thread allows an illusion of MIMD
    But with performance degredation
    Need to write general purpose code with care
 | Static: Discovered at Compile Time | Dynamic: Discovered at Runtime
Instruction-Level Parallelism | VLIW | Superscalar
Data-Level Parallelism | SIMD or Vector | Tesla Multiprocessor

## Slide 27: GPU Memory Structures
Notes: CUDA thread -> one iteration of a loop (with SIMD instructions
Thread block -> one vectorized loop
Grid -> vectorized loop made up of several thread blocks

## Slide 28: Putting GPUs into Perspective
Feature | Multicore with SIMD | GPU
SIMD processors | 4 to 8 | 8 to 16
SIMD lanes/processor | 2 to 4 | 8 to 16
Multithreading hardware support for SIMD threads | 2 to 4 | 16 to 32
Typical ratio of single precision to double-precision performance | 2:1 | 2:1
Largest cache size | 8 MB | 0.75 MB
Size of memory address | 64-bit | 64-bit
Size of main memory | 8 GB to 256 GB | 4 GB to 6 GB
Memory protection at level of page | Yes | Yes
Demand paging | Yes | No
Integrated scalar processor/SIMD processor | Yes | No
Cache coherent | Yes | No
Notes: Extreme data locality => only small caches are necessary.

## Slide 29: Guide to GPU Terms

## Slide 30: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors
§6.7 Clusters, WSC, and Other Message-Passing MPs

## Slide 31: Loosely Coupled Clusters
Network of independent computers
  Each has private memory and OS
  Connected using I/O system
    E.g., Ethernet/switch, Internet
Suitable for applications with independent tasks
  Web servers, databases, simulations, …
High availability, scalable, affordable
Problems
  Administration cost (prefer virtual machines)
  Low interconnect bandwidth
    c.f. processor/memory bandwidth on an SMP
Notes: A lot of supercomputers use message passing, but as one large system, vs. clusters…

## Slide 32: Sum Reduction (Again)
Sum 100,000 on 100 processors
First distribute 100 numbers to each
  The do partial sums
  sum = 0; for (i = 0; i<1000; i = i + 1) sum = sum + AN[i];
Reduction
  Half the processors send, other half receive and add
  The quarter send, quarter receive and add, …

## Slide 33: Sum Reduction (Again)
Given send() and receive() operations
  limit = 100; half = 100;/* 100 processors */ repeat half = (half+1)/2; /* send vs. receive dividing line */ if (Pn >= half && Pn < limit) send(Pn - half, sum); if (Pn < (limit/2)) sum = sum + receive(); limit = half; /* upper limit of senders */ until (half == 1); /* exit with final sum */
  Send/receive also provide synchronization
  Assumes send/receive take similar time to addition
Notes: There’s lots of details to how send() and receive() work
In real life you’d probably be using MPI

## Slide 34: Grid Computing
Separate computers interconnected by long-haul networks
  E.g., Internet connections
  Work units farmed out, results sent back
Can make use of idle time on PCs
  E.g., SETI@home, World Community Grid

## Slide 35: Interconnection Networks
Network topologies
  Arrangements of processors, switches, and links
§6.8 Introduction to Multiprocessor Network Topologies
Bus
Ring
2D Mesh
N-cube (N = 3)
Fully connected

## Slide 36: Multistage Networks

## Slide 37: Network Characteristics
Performance
  Latency per message (unloaded network)
  Throughput
    Link bandwidth
    Total network bandwidth
    Bisection bandwidth
  Congestion delays (depending on traffic)
Cost
Power
Routability in silicon
Notes: Fully connected total bandwidth: P(P-1)/2 (sum of (P-1)+(P-2)+(P-3)…+1+0)
Full connected bisection bandwith: (P/2)^2

## Slide 38: Parallel Benchmarks
Linpack: matrix linear algebra
SPECrate: parallel run of SPEC CPU programs
  Job-level parallelism
SPLASH: Stanford Parallel Applications for Shared Memory
  Mix of kernels and applications, strong scaling
NAS (NASA Advanced Supercomputing) suite
  computational fluid dynamics kernels
PARSEC (Princeton Application Repository for Shared Memory Computers) suite
  Multithreaded applications using Pthreads and OpenMP
§6.10 Multiprocessor Benchmarks and Performance Models

## Slide 39: Code or Applications?
Traditional benchmarks
  Fixed code and data sets
Parallel programming is evolving
  Should algorithms, programming languages, and tools be part of the system?
  Compare systems, provided they implement a given application
  E.g., Linpack, Berkeley Design Patterns
Would foster innovation in approaches to parallelism

## Slide 40: Modeling Performance
Assume performance metric of interest is achievable GFLOPs/sec
  Measured using computational kernels from Berkeley Design Patterns
Arithmetic intensity of a kernel
  FLOPs per byte of memory accessed
For a given computer, determine
  Peak GFLOPS (from data sheet)
  Peak memory bytes/sec (using Stream benchmark)

## Slide 41: Roofline Diagram
Attainable GPLOPs/sec
= Max ( Peak Memory BW × Arithmetic Intensity, Peak FP Performance )

## Slide 42: Comparing Systems
Example: Opteron X2 vs. Opteron X4
  2-core vs. 4-core, 2× FP performance/core, 2.2GHz vs. 2.3GHz
  Same memory system
To get higher performance on X4 than X2
  Need high arithmetic intensity
  Or working set must fit in X4’s 2MB L-3 cache

## Slide 43: Optimizing Performance
Optimize FP performance
  Balance adds & multiplies
  Improve superscalar ILP and use of SIMD instructions
Optimize memory usage
  Software prefetch
    Avoid load stalls
  Memory affinity
    Avoid non-local data accesses

## Slide 44: Optimizing Performance
Choice of optimization depends on arithmetic intensity of code
Arithmetic intensity is not always fixed
  May scale with problem size
  Caching reduces memory accesses
    Increases arithmetic intensity

## Slide 45: i7-960 vs. NVIDIA Tesla 280/480
§6.11 Real Stuff: Benchmarking and Rooflines i7 vs. Tesla

## Slide 46: Rooflines

## Slide 47: Benchmarks

## Slide 48: Performance Summary
GPU (480) has 4.4 X the memory bandwidth
  Benefits memory bound kernels
GPU has 13.1 X the single precision throughout, 2.5 X the double precision throughput
  Benefits FP compute bound kernels
CPU cache prevents some kernels from becoming memory bound when they otherwise would on GPU
GPUs offer scatter-gather, which assists with kernels with strided data
Lack of synchronization and memory consistency support on GPU limits performance for some kernels

## Slide 49: Multi-threading DGEMM
§6.12 Going Faster: Multiple Processors and Matrix Multiply
Use OpenMP:
void dgemm (int n, double* A, double* B, double* C)
{
#pragma omp parallel for
for ( int sj = 0; sj < n; sj += BLOCKSIZE )
for ( int si = 0; si < n; si += BLOCKSIZE )
for ( int sk = 0; sk < n; sk += BLOCKSIZE )
do_block(n, si, sj, sk, A, B, C);
}

## Slide 50: Multithreaded DGEMM

## Slide 51: Multithreaded DGEMM

## Slide 52: Fallacies
Amdahl’s Law doesn’t apply to parallel computers
  Since we can achieve linear speedup
  But only on applications with weak scaling
Peak performance tracks observed performance
  Marketers like this approach!
  But compare Xeon with others in example
  Need to be aware of bottlenecks
§6.13 Fallacies and Pitfalls

## Slide 53: Pitfalls
Not developing the software to take account of a multiprocessor architecture
  Example: using a single lock for a shared composite resource
    Serializes accesses, even if they could be done in parallel
    Use finer-granularity locking

## Slide 54: Concluding Remarks
Goal: higher performance by using multiple processors
Difficulties
  Developing parallel software
  Devising appropriate architectures
SaaS importance is growing and clusters are a good match
Performance per dollar and performance per Joule drive both mobile and WSC
§6.14 Concluding Remarks

## Slide 55: Concluding Remarks (con’t)
SIMD and vector operations match multimedia applications and are easy to program