## Slide 1: Dynamic Multiple-Issue (4.10)
Lecture 43
Notes: What did we look at yesterday?

## Slide 2: MIPS with Static Dual Issue
Notes: There’s a bug in this figure…what is it? (Need to add 8 to PC…)
Also, notice just one ALU above registers…(first, what is this for?) why don’t new need to replicate this?
Why doesn’t the bottom ALU need muxes?

## Slide 3: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 12($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 4($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 16($s1) | 5
 | addu $t3, $t4, $s2 | sw $t1, 12($s1) | 6
 | nop | sw $t2, 8($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 4($s1) | 8
Notes: What’s the IPC here?
Great, but what are the downsides?
Increased code size and more registers used…

## Slide 4: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 5: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s4, $s4, $t3 slti $t5, $s4, 20
  Can start sub while addu is waiting for lw
Notes: The only “dependence” is the t0 from lw to addu…
Actually, it’s often quite helpful to go through your instructions and explicitly write down the dependences
The dependence here is W->R, which is an important one
R->W is also an important one
R->R we don’t care about, as long as there is no write in between.
Example: the lw actually used t0 as the base address, then we don’t care that we use it for the addu…

## Slide 6: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands
Notes: This is a high-level overview. Lots more details. See Baer’s textbook.

## Slide 7: Register Renaming
Reservation stations and reorder buffer effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
    Register update may not be required

## Slide 8: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Don’t commit load until speculation cleared
Notes: Loads from RAM are way, way slower than everything else. Like, 100x slower.
We’ve acted like the memory is just the RAM, but that’s not actually true. We will see in the next chapter that it’s this thing called cache.

## Slide 9: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Can’t always schedule around branches
  Branch outcome is dynamically determined
Not all stalls are predictable
  e.g., cache misses
Different implementations of an ISA have different latencies and hazards
  Compiler would have to know about everything!
Notes: Scheduling around branch outcomes, obviously.
The caches, as we will see in the next chapter, let us make lw and sw much faster…except now always. Sometimes we have what’s called a “cache miss”, where we have to wait to load from slower memory. It’s really hard to predict ahead of time when this is going to happen, so static scheduling for multiple issue is not really an option.
Really hard to write a compiler that has to optimize for every possible architecture like this….

## Slide 10: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture

## Slide 11: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W
Notes: The downside is that if you want a single program to execute faster, you have to program it explicitly to use these extra cores…
… But doing so is actually really difficult. Making is easier is the focus of my research.

## Slide 12: Cortex A8 and Intel i7
Processor | ARM A8 | Intel Core i7 920
Market | Personal Mobile Device | Server, cloud
Thermal design power | 2 Watts | 130 Watts
Clock rate | 1 GHz | 2.66 GHz
Cores/Chip | 1 | 4
Floating point? | No | Yes
Multiple issue? | Dynamic | Dynamic
Peak instructions/clock cycle | 2 | 4
Pipeline stages | 14 | 14
Pipeline schedule | Static in-order | Dynamic out-of-order with speculation
Branch prediction | 2-level | 2-level
1st level caches/core | 32 KiB I, 32 KiB D | 32 KiB I, 32 KiB D
2nd level caches/core | 128-1024 KiB | 256 KiB
3rd level caches (shared) | - | 2- 8 MB
§4.11 Real Stuff: The ARM Cortex-A8 and Intel Core i7 Pipelines

## Slide 13: ARM Cortex-A8 Pipeline

## Slide 14: ARM Cortex-A8 Performance
Notes: We’ll see in chapter 5 that memory is very slow…

## Slide 15: Core i7 Pipeline
Notes: Ugh…don’t worry too much about this….
X86 makes pipelining difficult, so instead they take a micro-code approach…

## Slide 16: Core i7 Performance

## Slide 17: Matrix Multiply
Unrolled C code
1 #include <x86intrin.h>
2 #define UNROLL (4)
3
4 void dgemm (int n, double* A, double* B, double* C)
5 {
6 for ( int i = 0; i < n; i+=UNROLL*4 )
7 for ( int j = 0; j < n; j++ ) {
8 __m256d c[4];
9 for ( int x = 0; x < UNROLL; x++ )
10 c[x] = _mm256_load_pd(C+i+x*4+j*n);
11
12 for( int k = 0; k < n; k++ )
13 {
14 __m256d b = _mm256_broadcast_sd(B+k+j*n);
15 for (int x = 0; x < UNROLL; x++)
16 c[x] = _mm256_add_pd(c[x],
17 _mm256_mul_pd(_mm256_load_pd(A+n*k+x*4+i), b));
18 }
19
20 for ( int x = 0; x < UNROLL; x++ )
21 _mm256_store_pd(C+i+x*4+j*n, c[x]);
22 }
23 }
§4.12 Instruction-Level Parallelism and Matrix Multiply

## Slide 18: Matrix Multiply
Assembly code:
1 vmovapd (%r11),%ymm4 # Load 4 elements of C into %ymm4
2 mov %rbx,%rax # register %rax = %rbx
3 xor %ecx,%ecx # register %ecx = 0
4 vmovapd 0x20(%r11),%ymm3 # Load 4 elements of C into %ymm3
5 vmovapd 0x40(%r11),%ymm2 # Load 4 elements of C into %ymm2
6 vmovapd 0x60(%r11),%ymm1 # Load 4 elements of C into %ymm1
7 vbroadcastsd (%rcx,%r9,1),%ymm0 # Make 4 copies of B element
8 add $0x8,%rcx # register %rcx = %rcx + 8
9 vmulpd (%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
10 vaddpd %ymm5,%ymm4,%ymm4 # Parallel add %ymm5, %ymm4
11 vmulpd 0x20(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
12 vaddpd %ymm5,%ymm3,%ymm3 # Parallel add %ymm5, %ymm3
13 vmulpd 0x40(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
14 vmulpd 0x60(%rax),%ymm0,%ymm0 # Parallel mul %ymm1,4 A elements
15 add %r8,%rax # register %rax = %rax + %r8
16 cmp %r10,%rcx # compare %r8 to %rax
17 vaddpd %ymm5,%ymm2,%ymm2 # Parallel add %ymm5, %ymm2
18 vaddpd %ymm0,%ymm1,%ymm1 # Parallel add %ymm0, %ymm1
19 jne 68 <dgemm+0x68> # jump if not %r8 != %rax
20 add $0x1,%esi # register % esi = % esi + 1
21 vmovapd %ymm4,(%r11) # Store %ymm4 into 4 C elements
22 vmovapd %ymm3,0x20(%r11) # Store %ymm3 into 4 C elements
23 vmovapd %ymm2,0x40(%r11) # Store %ymm2 into 4 C elements
24 vmovapd %ymm1,0x60(%r11) # Store %ymm1 into 4 C elements
§4.12 Instruction-Level Parallelism and Matrix Multiply

## Slide 19: Performance Impact
Notes: But in reality, probably don’t unroll your loop unless you’re sure it will help.
Sometimes it will help, sometimes it will actually slow your code down due to cache stuff we will talk about later.
Compilers will do this automatically if you use –funroll-loop
The right way to program for performance is
Program to correctness and *clarity*
Profile your application, noting what the slow bottlenecks are
Improve those bottlenecks by rewriting and measuring your changes

## Slide 20: Fallacies
Pipelining is easy (!)
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends
    e.g., predicated instructions
§4.14 Fallacies and Pitfalls
Notes: We have really just scratched the surface (given an overview) or pipelining…

## Slide 21: Pitfalls
Poor ISA design can make pipelining harder
e.g., complex instruction sets (VAX, IA-32)
  Significant overhead to make pipelining work
  IA-32 micro-op approach
e.g., complex addressing modes
  Register update side effects, memory indirection
e.g., delayed branches
  Advanced pipelines have long delay slots

## Slide 22: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.14 Concluding Remarks