## Slide 1: 3.5: Finishing Floating Point
Lecture 34

## Slide 2: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102
Notes: Notice that rounding (say, 1.99999) may cause the number to become denormalized, so do step 3 again!

## Slide 3: FP Instructions in MIPS
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
    e.g., ldc1 $f8, 32($sp)
Floating point argument registers
  NOT $a1, $a2, etc.
  $f12, $f13, $f14, $f15
Floating point return value
  NOT $v0
  $f0

## Slide 4: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes (round to nearest even)
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements
Notes: Guard = first extra bit, round = second extra bit
3 significant bits, just a base 10 example for simplicity
Ex: 2.56 x 10^0 + 2.34 x 10^2, with and without guard and round
Another Ex: 5.01 x 10^-1, 2.34 x 10^2
Yields 0.0050 + 2.34 = 2.3450, need to set the sticky bit
Use sticky bit to round, since we often round to the nearest even

## Slide 5: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 6: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles
Patriot missile bug in 1991

## Slide 7: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
§3.9 Concluding Remarks

## Slide 8: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow
MIPS ISA
  Core instructions: 54 most frequently used
    100% of SPECINT, 97% of SPECFP
  Other instructions: less frequent

## Slide 9: Notes
Homework 4 walkthrough
Collaboration and academic dishonesty policies
Extra homework assignment
  10% correctness
  10% presentation effort
  80% a thorough, complete answer AND explanation
    A series of steps; why did you take each step?
    Even if your answer is wrong!

## Slide 10: The Processor
Chapter 4
Notes: What’s our master equation for performance?

## Slide 11: Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j
§4.1 Introduction