## Slide 1: Review
What are generate/propagate?

## Slide 2: A Plumbing Analog
Wrenches open and close valves
ci+1 will be full
  if the nearest generate value gi is on
  or pi is on there is water further upstream
c0 can result in a carry out without the help of any generates but the help of all propagates

## Slide 3: Review
What are generate/propagate?
Complicated for a large adder…how to fix?
Notes: Negating B and setting carryIn to 1.

## Slide 4: Four 4-bit ALUs with Carry Lookahead to form a 16-bit adder
Notes: Each of the boxes on the left is a 4-bit Carry lookahead adder (actually ALU).
Each computes their p and g, then their P and G and pass this to carry-lookahead unit.
Consider adding 16-bit
0001 1010 0011 0011
1110 0101 1110 1011

## Slide 5: Fast Carry Lookahead
How many “steps”?
step 1: produce generate and propagate
step 2: produce super generate and super propagate
step 3: produce carryout
much faster than adder without fast carry lookahead
Notes: Lots of other adders that work efficiently: carry-select, carry save

## Slide 6: Clocks
B.7

## Slide 7: Clock Cycle
Clock cycle time (clock period)
  Two portions
    Clock is high
    Clock is low
Edge-triggered clocking
  All state changes occur on a clock edge
Notes: Alternative is called level-triggered
State meaning we can read some input wire or write onto one, i.e., memory

## Slide 8: Combinational Logic and Sequential Logic
Combinational Logic
  A logic system whose blocks do not contain memory and hence compute the same output given the same input
    NOTE: So far EVERYTHING has been combinational logic.
Sequential Logic
  A group of logic elements that contain memory and hence whose value depends on the inputs as well as the current contents of the memory
    Made up of combinational logic and some memory

## Slide 9: State Element and Valid State
State Element
  A memory element
Signals written into state elements must be valid when the active clock edge occurs
  Valid means stable (not changing)
    Will not change again until the inputs change
Synchronous System
  A memory system that employs clocks and where data signals are read only when the clock indicates that the signal values are stable
Notes: Alternative is asynchronous systems, which can be very confusing.

## Slide 10
Inputs to a combinational logic block from a state element, and the outputs are written into a state element
Clock edge determines when the state elements are updated
Notes: Before first edge state element 1 could be in the process of changing. On first clock edge it is valid and can be read by combinational logic, which does some stuff during the clock cycle.
Then on the second edge this is valid and written to state element 2

## Slide 11: Read and Write in one cycle
Edge-triggered methodology allows a state element to be read and written in the same clock cycle
  Read the value of a state element
  Send it through some combinational logic
    Value does not change during the clock cycle
  Write it back to the same state element
  All in one cycle

## Slide 12: Memory Elements
Memory Elements
  Store States
  Output depends on
    The inputs, and
    The value stored in the memory element
Elements
  Flip-Flops
  Latches
  Registers
  Register Files
  SRAMS
  DRAMS
Notes: To store values for later, we need some type of feedback…This is pretty cool.

## Slide 13: Feedback
Notes: Q: Let’s say Q=0, S=1, R=0. What happens to Q?
Q: Q=1, S=0, R=1?

## Slide 14: Set-Reset Latch (S-R Latch)
A pair of cross-coupled NOR gates
  Unclocked
    Do not have a clock input
  Can store an internal value
    Q represent the current state

## Slide 15: S-R Latch (Cont.)
S=0 and R=0
  Previous State is stored
S=1 and R=0
  Q=1 and ~Q=0
S=0 and R=1
  Q=0 and ~Q=1
S=1 and R=1
  Q=0 and ~Q=0
  ???

## Slide 16: D-Latch
D-Latch
  Clock input C
  Data input D

## Slide 17: Difference btw. Latch and Flip-flop
Latch
  Asynchronous
    Output changes soon after input changes
Flip-flop
  Synchronous
    Output changes at the clock edge
Notes: A latch can be clocked or unclocked. The first S-R latch was unclocked and just changed whenever the input changed.
If clcocked, it changes when the clock is asserted/high.

## Slide 18: More on D-Latch
Q changes as D changes when clock is up
Not really edge-triggered
Notes: Basically, when the clock is high it immediately reacts to changes from D, then input.
Want edge-triggered to make sure everything is synchronized

## Slide 19: D Flip Flop
D Flip Flop with a Falling-Edge Trigger

## Slide 20: Setup Time and Hold Time
The input must be stable for a period of time before and after the clock edge
  Setup Time
    The minimum time the signal must be stable before clock edge
  Hold Time
    The minimum time the signal must be stable after clock edge
    Usually very small
Notes: We’re not going to talk much about these b/c we’re not really going to do much actual circuit design.

## Slide 21: Register Files
A register file consists of a set of registers that can be read and written by supplying a register number
  Built from an array of D Flip-Flops
  A decoder is used to select a register in the register file

## Slide 22: Reading Registers
Multiplexor
  Select data from the specific register

## Slide 23: Writing to a register
Write Signal
  Specify a write operation to the register
Decoder
  Specify which register to write
Register Data
  Data to write to the register

## Slide 24: Register Files
Register Files
  Can be used to build small memory
  Too costly to build large amount of memory
Large Scale Memory
  Static random access memories (SRAM)
  Dynamic random access memories (DRAM)

## Slide 25: SRAMs
SRAM
  Integrated circuits of memory arrays
  A single access port
    Either read or write
    Fixed access time to any datum
  Height
    Number of addressable locations
  Width
    Number of output bits per unit
Example: 8Mx8 SRAM
  8M = 223, 23 address lines
  8 output bits
Notes: Q: If I have 32 addressable locations, how many address lines do I need? A: 5 b/c 2^5 = 32.
Q: Now what if I have 8 MB? 1MB = 2^20 locations if each location is 1 byte. A: 23.

## Slide 26: 2Mx16 SRAM
21-bit address line
16-bit data input/output

## Slide 27: Implementation of Large SRAM
Register File
  Use Multiplexor
    32x1 Multiplexor
Large SRAM
  Impractical to use a large multiplexor like 64kx1
  Try to remember the implementation of a two input multiplexor
  Solution
    A more efficient implementation of Multiplexor
    Shared output line (bit line)
      Allow multiple sources to drive a single output line

## Slide 28: Small SRAM (4 x 2)

## Slide 29: Three State Buffer
  Two inputs
    A data signal
    An output enable (output select)
  A single output
    Three states
      Output enable = 1
        Asserted (1) state
        Deasserted (0) state
      Output enable = 0
        High Impedance state
        Allow the another three-state buffer with output enable =1 to determine the output

## Slide 30: Multiplexor using Three-State Buffers
Three-State Buffer
  Two inputs
    A data signal
    An output enable (output select)
  A single output
    Three states
      Output enable = 1
        Asserted (1) state
        Deasserted (0) state
      Output enable = 0
        High Impedance state
        Allow the another three-state buffer with output enable =1 to determine the output

## Slide 31: Organization of a 4M SRAM
Array of 8 Modules – Each for a bit
  Addr 21-10
    Use a 12 to 4096 decoder
    Select an array of1024 bits out of 4K 1024 bits
  Addr 9-0
    Select 1 bit from the 1024 bits as an output bit
Notes: So tristate buffers get rid of the problem of large multiplexors, but you’d still need large decoder and a whole lot of word lines. Instead we can use arrays of modules and a two step decode process.

## Slide 32: DRAM
SRAM
  Requires 4-6 transistors per bit
  Fast
  But costly
DRAM
  Requires 1 transistor per bit
  Charge stored in a capacitor
    Needs to be refreshed periodically
    Slower than SRAM
  But less expensive
Notes: Since it must be refreshed, it loses the values without power!

## Slide 33: Organization of a 4M DRAM
  Addr 11-21
    Select 1 row from 2048 rows
  Addr 10-0
    Select 1 bit from the 2048 bits as an output bit
  Column Latches
    Store the selected output from 2048x2048 array temporally
Notes: RAS (Row Access Strobe) and CAS(Column Access Strobe) to reduce lines needed.
Column latches also serve to help refresh, to latches and back.
Can also keep the values in the column latches and keep using new CAS values.
SDRAM is synchronous, i.e. clocked. That’s why you’ll see a speed, e.g. 3 GHz. (though they often will say 3000 or something)
DDR = double data rate, both rising and fall edge transfers

## Slide 34: DRAM

## Slide 35: SRAM and DRAM
SRAM
  Fast but costly
  Small amount
  Used for Computer Cache
DRAM
  Slow but less costly
  Large amount
  Used for Computer Main Memory

## Slide 36: What I want you to do
Read Appendix B.6-7