## Slide 1: Division
Instructor: Robert Utterback
Lecture 27
Notes: What instructions to we have for multiplication?
Mult, multu, mfhi, mflo, mul (pseudo)

## Slide 2: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low
Notes: “One cycle” assuming a single cycle for add…

## Slide 3: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel
Notes: Not correct! First Explain what this is trying so say.
Q: Do you see what’s wrong?
A: The left product bits cannot possibly be right…we must wait for the carry-in bits!
But there are more complicated schemes that can do better, see Booth’s algorithm and Wallace trees.
Can do in O(log n) time, but in practice still much slower than addition.

## Slide 4: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division
Notes: See if the divisor “fits” into the part of the dividend we’re looking at.
Except how does a computer know if it fits? If just checks if it’s less than, which it does by subtracting and checking < 0.

## Slide 5: Division Hardware
Initially dividend
Initially divisor in left half
First version of Division Hardware
  32-bit quotient
  64-bit ALU
  64-bit remainder
Notes: Note the similarity to multiplication HW:
Multiplicand * multiplier = product
Dividend = quotient * divisor + remainder -> Divisor * quotient = dividend - remainder
Divisor starts in left half of divisor register, remainder initialized to dividend

## Slide 6: First Version Division Hardware
Initially dividend
Initially divisor in left half
Notes: Shifting divisor to the right is basically considering another digit of dividend.
Example: Fill out a table for 7/2
Table:
Iteration, Step (1,2b,3), Quotient, Divisor, Remainder

## Slide 7
Iter | Step | Quotient | Divisor | Remainder
0 | Initial | 0000 | 0010 0000 | 0000 0111
1 | Rem = Rem - Div |  |  | 
 | Rem < 0? |  |  | 
 | Shift Div right |  |  | 
2 | Rem = Rem - Div |  |  | 
 | Rem < 0? |  |  | 
 | Shift Div right |  |  | 
3 | Rem = Rem - Div |  |  | 
 | Rem < 0? |  |  | 
 | Shift Div right |  |  | 
4 | Rem = Rem - Div |  |  | 
 | Rem < 0? |  |  | 
 | Shift Div right |  |  | 
5 | Rem = Rem - Div |  |  | 
 | Rem < 0? |  |  | 
 | Shift Div right |  |  | 
Notes: 7/2 Example.
Need n+1 iterations!

## Slide 8: Example
7/2
Notes: Need n+1 iterations.

## Slide 9: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both
Notes: Start: Dividend in right half, zeros in left half of “Remainder”
Remainder in left half, quotient in right half
The “one cycle” part is only if you adder only takes 1 cycle…may not be the case
Work out 7/2 example

## Slide 10
Iter | Step | Rem ¦ Quotient
0 | Initial | 
1 | Shift | 
 | Sub? | 
 | Q0=? | 
2 | Shift | 
 | Sub? | 
 | Q0=? | 
3 | Shift | 
 | Sub? | 
 | Q0=? | 
4 | Shift | 
 | Sub? | 
 | Q0=? | 
Notes: 7/2 Example.

## Slide 11: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT division) generate multiple quotient bits per step
  Still require multiple steps
Notes: Fastest I know of is O(log^2 n). In practice, 2-4x slower than mult?

## Slide 12: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result
Notes: Also div and divu with 3 registers: pseudoinstructions that give you the quotient
Also rem, and remu pseudoinstructions.

## Slide 13: Example Revisit
A better way to do 7/2?
  7>>2
  SRL
Most compiler will replace divide by power of 2 using right shift operations

## Slide 14: Summary
Multiplication
  First version of multiplication
  Optimized multiplication
Division

## Slide 15: 3.5: Floating Point
Notes: With integers, we could store all the values in a particular range. For real numbers, this is impossible. Why? Think about [0,1].
Instead, we’ve got to pick a representation that allows us to store some values spaced out in some range, hopefully to high enough precision that we can do scientific calculations.

## Slide 16: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point
Notes: Normalized: >= 1 < 10 (single digit before decimal point)

## Slide 17: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 18: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Not really, though
  Exponent is slightly more complicated
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Notes: Try an example on
Sign: 1
Exponent: 0 0 0 0 0 0 0 1
Fraction: 0 1 0 (0…)
Which is -1.25 * 2^1 = -2.5, except not really

## Slide 19: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Notes: Book’s terminology of fraction/mantissa vs. significand…not everyone uses them that way.
See p.200 for the reason behind biasing --- basically, it makes comparison a lot easier, hence sorting can be done efficiently.
The bias makes the most negative exponent (which makes a small number) 0…0 and the most positive exponent 1..1
Now example on p.201 (next slide)

## Slide 20: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 21: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Fxponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0