## Slide 1: Floating Point
Instructor: Robert Utterback
Lecture 28

## Slide 2: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point
Notes: Normalized: >= 1 < 10 (single digit before decimal point)

## Slide 3: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Notes: Book’s terminology of fraction/mantissa vs. significand…not everyone uses them that way.
See p.200 for the reason behind biasing --- basically, it makes comparison a lot easier, hence sorting can be done efficiently.
The bias makes the most negative exponent (which makes a small number) 0…0 and the most positive exponent 1..1
Now example on p.201 (next slide)

## Slide 4: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 5: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Fxponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 6: Floating-Point Numbers
Representation of floating point numbers in IEEE 754 standard:
single precision
1
8
23
sign
exponent:
excess 127
binary integer
Fraction (mantissa):
Hidden integer bit: 1.F
(actual exponent is e = E - 127)
S
E
F
Selection | Choices
A | - 1.010 * 2^130
B | 10
C | +10
D | 1.010 * 2^130
E | None of the above
Convert the following:
1 1000 0010 0100 0000 0000 0000 0000 000
Notes: Single precision example
Correct answer – B
Another example: convert 5.0 to floating point:
5.0 = 101 = 1.01 x 2^2
S=0,
Exp = 2 + 127 = 129 = 1000 0001
M = 01 0…
Result = 0 1000 0001 01 000000000000000000000

## Slide 7: Single-Precision Range
Exponents 00000000 and 11111111 reserved
“Smallest” value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 8: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 9: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
Notes: Let’s solve for this…How many decimal digits of precision?
2^23 = 10^x
log_10 2^23 = x
23 * log_10 2

## Slide 10: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision

## Slide 11: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52

## Slide 12: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 13: Denormal Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0
Two representations of 0.0!
Notes: How to represent 0?
See figure 3.13 on p.199 (next slide)
We have seen overflow, underflow is when the fraction part you are calculating became so small it can no longer be represented.
All 1 exponent and 0 fraction: Infinity! (positive or negative)
Use infinity for the result when dividing by 0.
All 1 exponent and nonzero fraction: NaN, for 0/0

## Slide 14: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 15: FP Encoding

## Slide 16: 3.5: Floating Point Arithmetic
Notes: In the book (and these slides), we’re basically just going to sketch the algorithms. There are actually a lot of details that go into actual floating point arithmetic that are tedious to deal with, but we just want to convey the main ideas.

## Slide 17: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
Notes: Consider a 4-digit decimal example
9.999 × 101 + 1.610 × 10–1
Q: How would you do it?

## Slide 18: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102
Notes: Notice that rounding (say, 1.99999) may cause the number to become denormalized, so do step 3 again!

## Slide 19: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2
Notes: Now let’s do a binary example (class exercise).
First, what are these numbers in base 10?
(0.5 + –0.4375)
So now we know what the answer *should* be…

## Slide 20: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1

## Slide 21: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
Notes: First, what are these numbers in base 10?
(0.5 + –0.4375)

## Slide 22: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
Notes: First, what are these numbers in base 10?
(0.5 + –0.4375)

## Slide 23: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625
Notes: First, what are these numbers in base 10?
(0.5 + –0.4375)

## Slide 24: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined (multiple adds in progress at same time)

## Slide 25: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4