## Slide 1: The Processor
Chapter 4
Notes: Note about collaboration…

## Slide 2: The Big Picture
The Five Classic Components of a Computer
Today’s Topic: Datapath Design, then Control Design
Control
Datapath
Memory
Processor
Input
Output
Notes: Before we go any further, let’s step back for a second and take a look at the big picture.
All computer consist of five components: (1) Input and (2) output devices. (3) The Memory System. And the (4) Control and (5) Datapath of the Processor.
Today’s lecture covers the datapath and control design.

## Slide 3: The Performance Perspective
Processor design (datapath and control) will determine:
  Clock cycle time
  Clock cycles per instruction
Starting today:
  Single cycle processor:
    Advantage: One clock cycle per instruction
    Disadvantage: long cycle time
ET = Insts * CPI * Cycle Time
Execute an
entire instruction
Notes: This slide shows how the next two lectures fit into the overall performance picture.
Have seen instruction count, now let’s dig into CPI (and also cycle time somewhat)
Instruction count is controlled by the Instruction Set Architecture and the compiler design so the computer engineer has very little control over it (Instruction Count).
What you as a computer engineer can control, while you are designing a processor, are the Clock Cycle Time and Instruction Count per cycle.
More specifically, in the next two lectures, you will be designing a single cycle processor which by definition takes one clock cycle to execute every instruction.
The disadvantage of this single cycle processor design is that it has a long cycle time.

## Slide 4: Simplified Processor
We're ready to look at an implementation of the MIPS simplified to contain only:
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, (and j later)
Generic Implementation:
  use program counter (PC) to supply instruction address
  get the instruction from memory
  read registers
  use the instruction to decide exactly what to do
Notes: Later we’ll look at a more realistic processor design.

## Slide 5: Instruction Execution
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4
Notes: These instructions actually have a lot in common. In particular, many need to read a register and use an ALU to calculate something.
Arithmetic need their result, load/store need to calculate memory address, beq must calculate instruction address…

## Slide 6: CPU Overview
Notes: Very basic diagram.
Q: What is top left add for? (get next instruction address)
Q: top right (branch calculation)
Assumes duplicated instruction and data memory, at least for now.

## Slide 7
Notes: Can’t just have multiple lines running into each other!
SQ: What logic component can we use to choose between multiple inputs?

## Slide 8: Multiplexers
Can’t just join wires together
  Use multiplexers
Notes: In addition to the muxers, we need to show how we decide which components to use, and how to use them.
e.g. do we take the PC+4 as next instruction, or the result of branch calculation?

## Slide 9: Control
Notes: We’ll show these “control” lines in blue.
Typically we won’t show all these control wires b/c they make the picture messy. Instead we’ll just show a blue line segment going in to the appropriate place at each block.
Q: What’s the AND gate at the top for? A: Must be branch instruction and result must have been true.

## Slide 10: Logic Design Basics
§4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information
Notes: Q: What is diff. between combinational and sequential logic?

## Slide 11: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 12: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 13: Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 14: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period
Notes: We have already seen this.
Right half is important b/c we want to be able to read and then write back to a register (e.g., add) in the same clock cycle.
Since this is a single-cycle CPU design, Q: What’s going to limit the cycle time of our clock? How fast can we make it?
A: Equal to the longest delay path through our logic.
Actually there are other factors: setup/hold time, clock skew, but we don’t worry too much about those.

## Slide 15: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 16: Instruction Fetch
32-bit register
Increment by 4 for next instruction
Notes: Q: Why do we need to increment by 4? So how big is the PC?

## Slide 17: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result
Notes: Q: Why 5 bits?

## Slide 18: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 19: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch
Notes: What addressing mode do branch instructions use?

## Slide 20: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 21: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions
Notes: Must first read the instruction before we know which addresses we need to read/write!

## Slide 22: R-Type/Load/Store Datapath

## Slide 23: Full Datapath

## Slide 24
Ignoring control - which instruction does this active datapath represent
R-type
lw
sw
Beq
None of the above
Active Single-Cycle Datapath
Notes: B

## Slide 25: ALU Control
ALU used for
  Load/Store: add
  Branch: subtract
  R-type: depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR
Notes: Why that relationship between add and subtract? Remember the picture of our ALU?
Need to generate these 4 ALU control bits based on the instruction we are currently executing..

## Slide 26: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111
Notes: Split into 3 groups:
Mem access op: 00
Branch: 01
Any R-type: 10

## Slide 27: Generating ALU signals
Main
Control
op
6
ALU
Control
func
2
6
ALUop
ALUctr
3
X: (Op1)(!Op0)(F0+F3)
Y: !Op1+!F2
Z: Op0+Op1F1
Select | ALUctr2 | ALUctr1 | ALUctr0
A | X | Y | Z
B | X | Z | Y
C | Y | Z | X
D | Z | Y | X
E | None of the above |  | 
Notes: This, then, is the logic. Notice that two function bits were dropped for being completely redundant (because of our small set of instructions).
Op0 is far-right bit, etc.
Answer: D

## Slide 28: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 29: Datapath With Control
Notes: E: Trace through an add, someone.

## Slide 30: Datapath With Control
Select | RegDst | MemToReg | ALUOp
A | 0 | X | 00
B | 1 | 0 | 00
C | 0 | X | 10
D | 1 | 0 | 10
E | None of the above |  | 
Notes: SQ: What are the control signals? A: D