## Slide 1: The Memory Hierarchy
Chapter 5

## Slide 2
From the book we know SRAM is very fast, expensive ($/GB), and small. We also know Disks are slow, inexpensive ($/GB), and large. Which statement best describes the role of cache when it works.
Selection | Role of caching
A | Locality allows us to keep frequently touched data in SRAM.
B | Locality allows us the illusion of memory as fast as SRAM but as large as a disk.
C | SRAM is too expensive to have large – so it must be small and caching helps use it well.
D | Disks are too slow – we have to have something faster for our processor to access.
E | None of these accurately describes the roll of cache.

## Slide 3: Cache Memory
§5.3 The Basics of Caches
Memory access
  How to tell if hit or miss?
Cache miss
  Where to put data?
  What to throw out?
  How to remember what data this is?

## Slide 4: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
How do we know if the data is present?
Where do we look?
Notes: Focus on these questions first.
Brainstorm some ideas on how to do this?

## Slide 5: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits
Notes: BTW, what’s the problem with this approach?
We may have two slots and also use two memory locations. Theoretically they should both fit in cache, but if they both map to the same slot they don’t!

## Slide 6: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0
Notes: Q

## Slide 7: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
Notes: First we are just going to think about reads.
Accesses:
22, 10 110
26, 11 010
22, 10 110
26, 11 010
16, 10 000
3, 00 011
16, 10 000
18, 10 010
16, 10 000

## Slide 8: Cache Example
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 9: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 10: Cache Example
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 

## Slide 11: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 12: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 13: Cache Example
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 

## Slide 14: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 15: Cache Example
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 

## Slide 16: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 17: Direct Mapped Cache
tag
data
4 blocks, each block holds one word, each word
in memory maps to exactly one cache location.
00 00 01 00
00 00 10 00
00 00 11 00
00 00 01 00
00 00 10 00
00 01 01 00
00 00 01 00
00 00 10 00
00 01 01 00
00 01 10 00
00 00 11 00
00 00 10 00
00 00 01 00
M
M
M
H
H
M
H
H
H
M M
H
M
M
M
M
H
H
M
M
H
H
M
H
H
H
M
M
M
H
H
M
M
H
M
M
H
M
M
M
H
M
H
H
M
H
H
H
M
H
H
M
A
B
C
D
E
None are correct
4
8
12
4
8
20
4
8
20
24
12
8
4
addresses
00
01
10
11
Notes: B

## Slide 18: Address Subdivision
Notes: Data can be grabbed in || with tag compare

## Slide 19: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
Notes: What block address? What block number?
In general, block addr = address / num blocks
Then mod by # blocks to get block number
Question: If you increase block size, how does that affect cache miss rate? More misses or fewer misses?
(at least, from small block sizes to larger)
A: fewer misses b/c of locality (but not too large, because then it causes conflicts)

## Slide 20: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 21: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access
Notes: OOO pipelines (superscalar) can actually get around this by executing other, non-dependent instructions…
If you’re reading, you basically might as well put it in the cache; you’re likely to need it again. The same is not necessarily true for writes…
Now: how to handle writes?

## Slide 22: Dealing with Writes
Stores must be handled differently than loads, because...
they don’t necessarily require the CPU to stall.
they change the content of cache/memory (creating memory consistency issues)
may require a _______ and a store to complete
Notes: There have been a number of issues glossed over – we’ll cover those now
May require a load if you want to bring into cache!

## Slide 23: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 24: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is “dirty”
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first