## Slide 1: Logical and Conditional Instructions
Instructor: Robert Utterback
Lecture 15

## Slide 2: Mini Green Sheet
MIPS instructions
  R:
  I:
Register numbers
  $t0 – $t7 : 8 – 15, $t8 – $t9 : 24 – 25
  $s0 – $s7 : 16 – 23, $zero : 0
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Notes: With a single exception, when op=0 it’s in R format

## Slide 3: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 4: Logical Operations (2.6)
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations

## Slide 5: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: We sometimes use this to get different bytes from a word.
Compare to base 10, multiplying by 10

## Slide 6: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 7: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 8: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 9: Making Decisions (2.7)

## Slide 10: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 11: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …
Assembler calculates addresses

## Slide 12: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 13: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 14: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 15: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise
Notes: How to do >? What about <=?

## Slide 16: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0